| Title | Use and maintain hand and power tools for electrical work |
| --- | --- |
| Level | 3 | Credits | 3 |

| Purpose | This unit standard covers the use and maintenance of hand and power tools commonly used during installation and maintenance work in the electrical and related industries. People credited with this unit standard are able to: – use hand tools safely for electrical work – maintain hand tools – use power tools safely for electrical work – maintain power tools. |
| --- | --- |

| Classification | Electrical Engineering > Core Electrical |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	This unit standard has been developed for learning and assessment on-job.

2	Definitions

RCD – residual current device

Safe and sound practice – as it relates to the installation of electrical equipment is defined in AS/NZS 3000 (version as cited in Electricity (Safety) Regulations), Electrical Installations (known as the Australian/New Zealand Wiring Rules).

3	Range

a	Hand tools may include but are not limited to – knife, cold chisel, wood chisel, hacksaw, wood saw, hole-saw, file, twist drill bits, auger drill bits, high-speed wood bits, rule, tape measure, adjustable and fixed spanners, socket sets, Allen keys, spline-driver, combination pliers, long-nose pliers, side cutters (diagonal cutters), vice-grips, poly-grips (multi-grips), screwdrivers (flat, Phillips, Square-drive and Posi-Drive), hammer, crimp tool; evidence of 15 required.

b	Power tools may include but are not limited to – electric drill, portable electric saw, bench grinder, angle grinder, cordless screwdriver, cordless drill.  Evidence of four required.

c	Candidates may refer to current legislation and Standards during assessment.

d	Demonstration of safe working practices and installation in accordance with safe and sound practice are essential components of assessment of this unit standard.

e	All activities and evidence presented for all outcomes and performance criteria in this unit standard must be in accordance with:

i	legislation

ii	policies and procedures

iii	ethical codes

iv	Standards – may include but are not limited to those listed in Schedule 2 of the Electricity (Safety) Regulations 2010

v	applicable site, enterprise, and industry practice

vi	where appropriate, manufacturers’ instructions, specifications, and data sheets.

Outcomes and performance criteria

Outcome 1

Use hand tools safely for electrical work.

Performance criteria

1.1	Select hand tools according to work requirements.

Range	may include but is not limited to – tool function, length, weight, opening width, blade width, tool type;

work requirements – size and type of material, risk of damage to the work.

1.2	Use hand tools safely.

1.3	Take additional precautions when hand tools are used near live equipment and ensure that they are adequately insulated.

Outcome 2

Maintain hand tools.

Performance criteria

2.1	Maintain hand tools in terms of cleaning, lubricating, sharpening, storage, and protection against damage.

2.2	Inspect hand tools regularly for signs of wear and repair or discard when damaged.

Outcome 3

Use power tools safely for electrical work.

Performance criteria

3.1	Check power tools for safety and wear before use.

Range	checks may include but are not limited to – frayed or damaged flexible cords, integrity of appliance connector or plug tops, pins straight, screws tight, cord grips functioning, integrity of casings, missing parts, damaged components, lubrication.

3.2	Select power tools for cutting and drilling applications to match the size, nature, and environment of the task to be performed.

3.3	Use power tools in accordance with manufacturers' specifications, industry practice, and safety requirements without damage to the tool, the material on which they are used, or personnel.

3.4	Use isolating transformers or RCDs with tools operating at mains voltage.

Outcome 4

Maintain power tools.

Performance criteria

4.1	Keep power tools in a state of good repair and protected from damage.

4.2	Coil and store cords and, where appropriate, hoses in a manner that avoids strain, twists, and kinks.

| Replacement information | This unit standard replaced unit standard 1175 and unit standard 5919. |
| --- | --- |

| Planned review date | 31 December 2025 |
| --- | --- |

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 28 June 1999 | 31 December 2013 |
| Revision | 2 | 3 April 2001 | 31 December 2013 |
| Review | 3 | 26 May 2005 | 31 December 2021 |
| Rollover and Revision | 4 | 15 March 2012 | 31 December 2021 |
| Revision | 5 | 15 January 2014 | 31 December 2021 |
| Review | 6 | 21 July 2016 | N/A |
| Revision | 7 | 16 March 2017 | N/A |
| Rollover and Revision | 8 | 25 May 2023 | N/A |

| Consent and Moderation Requirements (CMR) reference | 0003 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.

Comments on this unit standard

Please contact Waihanga Ara Rau Construction and Infrastructure Workforce Development Council qualifications@WaihangaAraRau.nz if you wish to suggest changes to the content of this unit standard.