| Title | Install resilient sheet floorcoverings |
| --- | --- |
| Level | 4 | Credits | 35 |

| Purpose | People credited with this unit standard are able to: confirm flooring job and specifications and select equipment; carry out installation of resilient floorcoverings; maintain a safe working environment; and complete job records. |
| --- | --- |

| Classification | Construction Trades > Flooring |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Performance of the outcomes of this unit standard must comply with the following legislation and guides: the Building Act 2004; Health and Safety in Employment Act 1992; A Guide to the Health and Safety in Employment Act 1992 (2003 – 2nd edition), published by the Department of Labour and available at http://www.osh.dol.govt.nz; and their subsequent amendments.

2	Workplace procedures are all authorised instructions, processes and work practices carried out in the workshop, factory, shop and worksite.

3	Assessment against this unit standard must take place in a commercially acceptable timeframe.

Outcomes and performance criteria

Outcome 1

Confirm flooring job and specifications and select equipment.

Performance criteria

1.1	Job is confirmed to be consistent with job sheet in accordance with workplace procedures.

Range	includes but is not limited to – client name, location, access, area, environment.

1.2	Job specifications are confirmed to be consistent with client’s requirements and job sheet.

1.3	Material supplied is checked for its consistency with the material specifications.

1.4	Equipment is selected in accordance with the job specifications.

Range	includes but is not limited to – tools, fire extinguisher, applicators, vacuum cleaner, thermo welder, air compressor, heat gun, router, spray guns, sealant gun, space heater.

Outcome 2

Carry out installation of resilient floorcovering.

Performance criteria

2.1	Resilient floorcovering is cut to meet the requirements of the manufacturers’ specifications and the workplace procedures.

2.2	Adhesives applied meet the requirements of the product and the method of installation used.

Range	includes but is not limited to – positioning, open and tack times, adhesion transfer.

2.3	Placement of the floorcovering meets the manufacturers’ specifications and workplace procedures.

2.4	Seaming methods used meet the manufacturers’ specifications and workplace procedures.

Range	includes but is not limited to – double cut, recess scribing, thermo-welding, chemical weld.

Outcome 3

Maintain a safe working environment.

Performance criteria

3.1	Work practices are carried out without injury to people or damage to equipment, building, or plant, in accordance with workplace procedures.

3.2	Personal protective equipment for the task at hand is selected and worn in accordance with manufacturers’ specifications.

Range	includes but is not limited to – ear muffs, safety glasses, gloves, mask, knee pads.

3.3	Safety notices are distributed, and signs bearing notification of work are erected in accordance with workplace procedures.

3.4	Work area is kept clear of debris and unwanted items in accordance with workplace procedures.

Outcome 4

Complete job records.

Performance criteria

4.1	Job sheets are completed in accordance with workplace procedures.

4.2	Records are stored in accordance with workplace procedures.

| Replacement information | This unit standard, unit standard 16999, unit standard 17000, and unit standard 17001 replaced unit standard 9780. |
| --- | --- |

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 29 May 2000 | 31 December 2023 |
| Revision | 2 | 18 February 2004 | 31 December 2023 |
| Review | 3 | 26 March 2007 | 31 December 2024 |
| Review | 4 | 25 November 2021 | 31 December 2024 |
| Rollover | 5 | 30 November 2023 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0175 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.