| Title | Install carpet by conventional method |
| --- | --- |
| Level | 4 | Credits | 25 |

| Purpose | People credited with this unit standard are able to: confirm flooring job and specifications and select equipment; carry out carpet installation; maintain a safe working environment; and complete job records. |
| --- | --- |

| Classification | Construction Trades > Flooring |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Performance of the outcomes of this unit standard must comply with the following legislation and guides: the Building Act 2004; Health and Safety in Employment Act 1992; A Guide to the Health and Safety in Employment Act 1992 (2003 – 2nd edition), published by the Department of Labour and available at http://www.osh.dol.govt.nz; and their subsequent amendments.

2	Workplace procedures are all authorised instructions, processes and work practices carried out in the workshop, factory, shop and worksite.

3	Assessment against this unit standard must take place in a commercially acceptable timeframe.

Outcomes and performance criteria

Outcome 1

Confirm flooring job and specifications and select equipment.

Performance criteria

1.1	Job is confirmed to be consistent with job sheet in accordance with workplace procedures.

Range	includes but is not limited to – client name, location, access, area, environment.

1.2	Job specifications are confirmed to be consistent with client’s requirements and job sheet.

1.3	Material supplied is checked for its consistency with the material specifications.

  - Equipment is selected in accordance with the job specifications.

Range	equipment includes but is not limited to – hand tools, staples, heat seaming equipment, power stretcher, knee-kicker, trimmers, adhesive applicators, vacuum cleaner.

Outcome 2

Carry out carpet installation.

Performance criteria

2.1	Fastening systems, underlayments, adhesives, seam bonds and seals are applied in accordance with manufacturers’ specifications and workplace procedures.

2.2	Installation complies with manufacturers’ specifications.

Outcome 3

Maintain a safe working environment.

Performance criteria

3.1	Work practices are carried out without injury to people or damage to equipment, building, or plant, in accordance with workplace procedures.

3.2	Personal protective equipment for the task at hand is selected and worn in accordance with manufacturers’ specifications.

Range	may include but is not limited to – ear muffs, safety glasses, gloves, mask, knee pads.

3.3	Safety notices are distributed, and signs bearing notification of work are erected in accordance with workplace procedures.

3.4	Work area is kept clear of debris and unnecessary equipment in accordance with workplace procedures.

Outcome 4

Complete job records.

Performance criteria

4.1	Job sheets are completed in accordance with workplace procedures.

4.2	Records are stored in accordance with workplace procedures.

| Replacement information | This unit standard and unit standard 10846 were replaced by unit standard 32527. This unit standard, unit standard 17005, and unit standard 17006 replaced unit standard 10844. |
| --- | --- |

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 29 May 2000 | 31 December 2023 |
| Revision | 2 | 18 February 2004 | 31 December 2023 |
| Review | 3 | 26 March 2007 | 31 December 2024 |
| Review | 4 | 25 November 2021 | 31 December 2024 |
| Rollover | 5 | 30 November 2023 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0175 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.