| Title | Install laminated timber flooring overlays |
| --- | --- |
| Level | 4 | Credits | 20 |

| Purpose | This unit standard is for experienced people working in the timber flooring sector of the industry. People credited with this unit standard are able to: confirm flooring job and specifications and select equipment; install laminated timber flooring overlays; maintain a safe working environment; and complete job records. |
| --- | --- |

| Classification | Construction Trades > Flooring |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Performance of the outcomes of this unit standard must comply with the following legislation and guides: the Building Act 2004; Health and Safety in Employment Act 1992; A Guide to the Health and Safety in Employment Act 1992, 2nd edition (Department of Labour, 2003) available at http://www.osh.dol.govt.nz; and their subsequent amendments.

2	Definition

Workplace procedures are all authorised instructions, processes and work practices carried out in the workshop, factory, shop and worksite.

3	The range for the whole standard is both floating timber flooring overlays and adhered timber flooring overlays.

4	This unit standard must be assessed in a realistic workplace environment.  The candidate must be under realistic time pressures, use relevant commercial equipment, and have realistic staff ratios.  Commercially acceptable timeframes vary for the different flooring installation sectors.

Outcomes and performance criteria

Outcome 1

Confirm flooring job and specifications and select equipment.

Performance criteria

1.1	Job is confirmed to be consistent with job sheet in accordance with workplace procedures.

Range	includes but is not limited to – client name, location, access, area, environment.

1.2	Job specifications are confirmed to be consistent with client’s requirements and job sheet.

1.3	Material supplied is checked for its consistency with the material specifications.

1.4	Equipment is selected in accordance with the job specifications.

Range	equipment includes but is not limited to – hand tools, vacuum cleaner, powered saws, router, drills, planers, levels, straight edges, trowels, sandbags.

Outcome 2

Install laminated timber flooring overlays.

Performance criteria

2.1	Surfaces are checked to ensure that they meet covering product manufacturers’ specifications.

Range	includes but is not limited to – level, texture of surface, absence of foreign materials.

2.2	Area is cordoned off in accordance with workplace procedures.

2.3	Overlays are laid in accordance with manufacturers’ specifications and workplace procedures.

Outcome 3

Maintain a safe working environment.

Performance criteria

3.1	Work practices are carried out without injury to people or damage to equipment, building, or plant, in accordance with workplace procedures.

3.2	Personal protective equipment for the task at hand is selected and worn in accordance with manufacturers’ specifications and workplace procedures.

Range	includes but is not limited to – ear muffs, safety glasses, gloves, mask, knee pads.

3.3	Safety notices are distributed, and signs bearing notification of work are erected in accordance with workplace procedures.

3.4	Work area is kept clear of debris and unwanted items in accordance with workplace procedures.

Outcome 4

Complete job records.

Performance criteria

4.1	Job sheets are completed in accordance with workplace procedures.

4.2	Records are stored in accordance with workplace procedures.

| Replacement information | This unit standard and unit standard 17012 were replaced by unit standard 32536. |
| --- | --- |

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 29 May 2000 | 31 December 2013 |
| Revision | 2 | 18 February 2004 | 31 December 2013 |
| Review | 3 | 26 March 2007 | 31 December 2013 |
| Review | 4 | 18 February 2011 | 31 December 2024 |
| Review | 5 | 25 November 2021 | 31 December 2024 |
| Rollover | 6 | 30 November 2023 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0175 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.