| Title | Examine and evaluate substrate in the flooring industry |
| --- | --- |
| Level | 4 | Credits | 12 |

| Purpose | This unit standard is for experienced people working in the flooring industry. People credited with this unit standard are able to: confirm flooring job and specifications; carry out examination of flooring substrate; and carry out evaluation of substrate conditions. |
| --- | --- |

| Classification | Construction Trades > Flooring |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Performance of the outcomes of this unit standard must comply with the following legislation and guides: the Building Act 2004; Health and Safety in Employment Act 1992; A Guide to the Health and Safety in Employment Act 1992, 2nd edition (Department of Labour, 2003) available at http://www.osh.dol.govt.nz; New Zealand Standard NZS 3114:1987 Specification for concrete surface finishes guidelines, available at http://www.standards.co.nz.

2	Definition

Workplace procedures are all authorised instructions, processes and work practices carried out in the workshop, factory, shop and worksite.

3	The report on the state of the substrate may include a recommended course of action.

Outcomes and performance criteria

Outcome 1

Confirm flooring job and specifications.

Performance criteria

1.1	Job is confirmed to be consistent with job sheet in accordance with workplace procedures.

Range	includes but is not limited to – client name, location, access, area, environment.

1.2	Job specifications are confirmed to be consistent with client’s requirements and job sheet.

Outcome 2

Carry out examination of flooring substrate.

Performance criteria

2.1	Equipment selected meets the requirements of the examination method and the manufacturers’ specifications.

Range	equipment may include but is not limited to – moisture meters, levels, string lines, hardness tester, core frilling, pull-off tester.

2.2	Examination method used meets the requirements of the job and the workplace procedures.

Range	checks may include but are not limited to – surface condition, moisture level, surface contaminants, fall and levels, hardness, tolerances, control joint evaluation, stability, deflection.

2.3	Results of the examination are recorded in accordance with workplace procedures.

Outcome 3

Carry out evaluation of substrate conditions.

Performance criteria

3.1	Evaluation includes examination of substrate conditions in accordance with workplace procedures.

Range	may include but is not limited to – moisture content, falls and levels, strength of substrate, contamination, age of cure.

3.2	Results of evaluation are recorded in accordance with workplace procedures.

Range	includes but is not limited to – report format, content.

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 29 May 2000 | 31 March 2017 |
| Revision | 2 | 18 February 2004 | 31 March 2017 |
| Review | 3 | 26 March 2007 | 31 March 2017 |
| Review | 4 | 18 February 2011 | 31 December 2024 |
| Review | 5 | 25 November 2021 | 31 December 2024 |
| Rollover | 6 | 30 November 2023 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0175 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.