| Title | Install and finish decorative exterior mouldings to Proprietary Plaster Cladding Systems on site |
| --- | --- |
| Level | 3 | Credits | 8 |

| Purpose | People credited with this unit are able to: identify and order decorative mouldings in accordance with job specifications; prepare and install decorative mouldings on site; and complete joint finishing and edge sealing of decorative mouldings on site. |
| --- | --- |

| Classification | Construction Trades > Proprietary Plaster Cladding Systems |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Definitions

On site refers to a wide range of building and construction environments within which the Proprietary Plaster Cladding Systems trade skills are applied.

Specifications refers to documented instructions (oral, written, graphic) and may include any of the following:  manufacturer’s specifications, recommendations or technical data sheets; material specifications; specifications from a specialist source such as an architect, designer, engineer or a supervisor; site or work specific requirements.

Work site practice refers to the documented procedures specific to a work site, which set out the standard and required practices of that work site.

2	Legislation, regulations, codes and standards relevant to this unit standard include:

Health and Safety in Employment Act 1992;

Health and Safety in Employment Regulations 1995;

Resource Management Act 1991;

Hazardous Substances and New Organisms Act 1996; Building Act 2004;

New Zealand Standards, NZS 4218:2004 Energy efficiency – Small building envelope and NZS 3604:1999 Timber Framed Buildings, available from Standards NZ (http://www.standards.co.nz);

New Zealand Building Code;

Territorial Authorities’ building regulations.

3	Credit for this unit standard indicates compliance with industry practice.  Industry practice refers to the ability to demonstrate knowledge and skills that reflect the productivity, uniformity, finish quality and material economies currently accepted within industry.

Outcomes and performance criteria

Outcome 1

Identify and order decorative mouldings in accordance with job specifications.

Range	designer’s and owner’s requirements.

Performance criteria

1.1	Work to be done is determined from plans, working drawings and specifications in terms of types of decorative mouldings, materials and workmanship to be used.

1.2	The range of moulding options available is identified and their applications in different situations are described.

Range	two of – uncoated polystyrene, polyurethane, premeshed, precoated.

1.3	The sizing, measuring and ordering process for mouldings is identified and described in relation to job specifications.

1.4	The ordering, receipt, checking, and site storage of decorative mouldings and fixings are undertaken in accordance with job specifications and work site practice.

Range	confirmation of delivered materials, return or replacement of defective materials, use of appropriate handling and storage methods to prevent damage.

Outcome 2

Prepare and install decorative mouldings on site.

Performance criteria

2.1	Surface area layout for decorative mouldings is prepared and confirmed against plans, working drawings and job specifications.

Range	tools used include two of – string lines, plumb lines, level lines, chalk lines, laserlines.

2.2	Actions to be taken in the event that the fixing surfaces are not in accordance with a plan, specifications, or work site practice, are described.

Range	cleaning, levelling, straightening

2.3	Cuts and mitres for decorative mouldings are completed to meet manufacturer’s instructions, job specifications and work site practice.

Range	tools used – hand saw, power saw.

2.4	Fixing methods used with decorative mouldings are identified and confirmed against the manufacturer’s instructions and job specifications.

Range	two of – mechanical fasteners, adhesives, modified plaster.

2.5	Decorative mouldings are installed and fixed in accordance with manufacturer’s instructions and job specifications.

Outcome 3

Complete joint finishing and edge sealing of decorative mouldings on site.

Range	two of – plastering, mesh reinforcing, sealants.

Performance criteria

3.1	Joint finishing of decorative mouldings is completed in accordance with manufacturer’s instructions and without damage.

3.2	Edge sealing of decorative mouldings is completed in accordance with manufacturer’s instructions and without damage.

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 23 June 2000 | 31 December 2024 |
| Review | 2 | 24 January 2006 | 31 December 2024 |
| Review | 3 | 26 January 2007 | 31 December 2024 |
| Review | 4 | 30 June 2022 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0048 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.