| Title | Demonstrate knowledge of and fix curved plaster board on site |
| --- | --- |
| Level | 4 | Credits | 10 |

| Purpose | People credited with this unit standard are able to describe methods used to fix curved plaster board on site, and fix curved wall and ceiling areas on site. |
| --- | --- |

| Classification | Construction Trades > Plaster Board |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

| Prerequisites | Unit 6120, Demonstrate knowledge of and fix flat plaster board to level and sloping ceilings on site; and Unit 6121, Demonstrate knowledge of and fix flat plaster board to walls on site; or demonstrate equivalent knowledge and skills. |
| --- | --- |

Guidance Information

1	Definitions

Access equipment, for the purpose of this unit standard, means equipment used to facilitate access to the work area, and may include ladders, working platforms, scaffolding or mechanical plant.  Approved codes of practice relating to the safe operation of this equipment are available at http://www.osh.govt.nz.

On site refers to a wide range of building and construction environments within which trade skills are applied.

Specifications refers to documented instructions (oral, written, graphic) and may include any of the following:  manufacturer’s specifications, recommendations or technical data sheets; material specifications; specifications from a specialist source such as an architect, designer, engineer or a supervisor; site or work specific requirements.

Work site practice refers to the documented procedures specific to a work site, which set out the standard and required practices of that work site.

2	All work practices must comply with the following:

Health and Safety in Employment Act 1992 and Health and Safety in Employment Regulations 1995; Resource Management Act 1991; Building Act 2004; AS/NZS 2589:2007 Gypsum linings - Application and finishing, available from Standards NZ (http://www.standards.co.nz); Approved Code of Practice for the Safe Erection and Use of Scaffolding (Wellington: Occupational Safety and Health Service, Department of Labour, 1995) available at http://www.osh.govt.nz.

3	Credit for this unit standard indicates compliance with industry practice.  Industry practice refers to the ability to demonstrate knowledge and skills that reflect the productivity, uniformity, finish quality and material economies currently accepted within industry.

Outcomes and performance criteria

Outcome 1

Describe methods used to fix curved plaster board on site.

Range	concave, convex.

Performance criteria

1.1	Methods of fixing are described in accordance with manufacturer’s and job specifications.

Outcome 2

Fix curved wall and ceiling areas on site.

Range	on site environments include – residential, commercial, industrial, multi-storey;

one environment is required.

Performance criteria

2.1	Access equipment is arranged in accordance with the Health and Safety in Employment Regulations.

2.2	Surfaces to be lined are checked as fit for purpose for sheet placement.

2.3	Sheet set-out is determined using factors identified as affecting the end result.

Range	critical light, natural and artificial light conditions, specified finishes, design factors.

2.4	Sheets are set out and cut to suit curve and manufacturer’s recommendations.

2.5	Sheets are fixed to achieve required curve in accordance with the manufacturer’s recommendations.

2.6	All operations are completed, workplace and tools cleaned, and tools stored in accordance with work site practice.

| Replacement information | This unit standard and unit standard 17582 replaced unit standard 4333. |
| --- | --- |

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 29 August 2000 | 31 December 2024 |
| Revision | 2 | 18 May 2005 | 31 December 2024 |
| Review | 3 | 20 April 2006 | 31 December 2024 |
| Review | 4 | 25 January 2008 | 31 December 2024 |
| Review | 5 | 26 May 2022 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0048 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.