| Title | Fix flat fibrous plaster sheets to surfaces |
| --- | --- |
| Level | 2 | Credits | 8 |

| Purpose | People credited with this unit standard are able to fix flat fibrous plaster sheets to surface areas, and clean up after work is completed. |
| --- | --- |

| Classification | Construction Trades > Fibrous Plaster |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Credit for this unit standard can be achieved on site through a registered assessor, or off site with an accredited training provider.

2	All work practices must comply with the following:

Health and Safety in Employment Act 1992;

Health and Safety in Employment Regulations 1995;

Resource Management Act 1991;

Building Act 2004;

AS/NZS 2589:2007 Gypsum linings – Application and finishing, available from Standards NZ (http://www.standards.co.nz);

Approved Code of Practice for the Safe Erection and Use of Scaffolding (Wellington: Occupational Safety and Health Service, Department of Labour, 1995) available at http://www.osh.govt.nz;

New Zealand Building Code.

Outcomes and performance criteria

Outcome 1

Fix flat fibrous plaster sheets to surface areas.

Performance criteria

1.1	Access is arranged and complies with the Health and Safety in Employment Regulations 1995.

1.2	Sheet sizes are determined from work measure and order list.

1.3	Sheets are trimmed for jointing methods specified, projections and recesses.

1.4	Temporary support systems are selected and used as required by the site conditions.

1.5	Sheets are fixed to framing or backing as specified by manufacturer.

Range	nails, screws, adhesives, wadding; combination.

1.6	All operations are completed without damage to the workplace, tools or plant.

Outcome 2

Clean up after work is completed.

Performance criteria

2.1	Tools and plant are maintained, cleaned and stored in accordance with site practice.

2.2	Waste material is disposed of and workplace is cleaned in accordance with site practice.

| Replacement information | This unit standard replaced unit standard 4320 and unit standard 4321. |
| --- | --- |

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 29 August 2000 | 31 December 2024 |
| Revision | 2 | 18 May 2005 | 31 December 2024 |
| Review | 3 | 20 April 2006 | 31 December 2024 |
| Revision | 4 | 25 January 2008 | 31 December 2024 |
| Review | 5 | 26 May 2022 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0048 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.