| Title | Cut glass with an automated or semi-automated machine |
| --- | --- |
| Level | 4 | Credits | 10 |

| Purpose | This unit standard is for experienced people in the glass processing industry. People credited with this unit standard are able to select glass and prepare glass for cutting, and cut glass using an automated or semi-automated machine. |
| --- | --- |

| Classification | Glass and Glazing > Glass Processing and Manufacturing |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Definition

Worksite requirements – refer to instructions to staff on policy and procedures which are documented in memo or manual format and are available in the workplace.  These requirements include – company specifications and procedures, work instructions, manufacturer’s specifications, product quality specifications, legislative requirements.

2	Legislation relevant to this unit standard includes – Health and Safety at Work Act 2015.

Outcomes and performance criteria

Outcome 1

Select glass and prepare glass for cutting.

Performance criteria

1.1	Preparation of work area and personal safety precautions are carried out in accordance with worksite requirements.

Range	preparation includes – selection and use of protective clothing and safety equipment, identification of hazards, ventilation of production area, clearing work area, ensuring cleanliness of work area.

1.2	Glass is selected to meet the job specifications for type, thickness, and size and is checked for imperfections before use in accordance with worksite requirements.

Outcome 2

Cut glass using an automated or semi-automated machine.

Performance criteria

2.1	Machine is set up in accordance with the job specifications and worksite requirements.

Range	set-up includes – loader settings, cutting machine settings.

2.2	Machine is operated in accordance with worksite requirements.

Range	operation includes – loading, cutting, unloading, dealing with off-cuts and trims.

2.3	Cut glass is checked for compliance with the job specifications.

2.4	Procedures are applied to finished glass in accordance with worksite requirements.

Range	procedures include – cleaning, labelling or marking, stacking, storing, preparation for further processing or dispatch.

| Replacement information | This unit standard replaced unit standard 2061. |
| --- | --- |

| Planned review date | 31 December 2022 |
| --- | --- |

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 27 April 2004 | 31 December 2013 |
| Review | 2 | 21 May 2010 | 31 December 2017 |
| Review | 3 | 18 June 2015 | N/A |
| Rollover and Revision | 4 | 25 August 2022 | N/A |

| Consent and Moderation Requirements (CMR) reference | 0073 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.

Comments on this unit standard

Please contact Hanga-Aro-Rau Manufacturing, Engineering and Logistics Workforce Development Council at qualifications@hangaarorau.nz if you wish to suggest changes to the content of this unit standard.