| Title | Install floor and wall tiles on site |
| --- | --- |
| Level | 4 | Credits | 20 |

| Purpose | People credited with this unit standard are able to: demonstrate knowledge of tile installation, cut tiles on site, install floor and wall tiles on site, and complete work operations. |
| --- | --- |

| Classification | Construction Trades > Floor and Wall Tiling |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Definitions

Sealant refers to flexible joint filler that is applied to movement joints within tiling jobs.

Sealers refers to a substance applied as a coating to tiles to protect from staining and moisture.

Specifications refers to documented instructions (oral, written, graphic) and may include any of the following: manufacturer’s specifications, recommendations or technical data sheets; material specifications; specifications from a specialist source such as an architect, designer, engineer or a supervisor; site or work specific requirements.

Wet area refers to any area exposed to moisture that requires waterproofing, for example bathrooms or laundries.

Work site practice refers to the documented procedures specific to a work site which set out the standard and required practices of that work site.

2	Credit for this unit standard indicates compliance with industry practice.  Industry practice refers to the ability to work unsupervised, demonstrating knowledge and skills that reflect the productivity, uniformity, finish quality and material economies currently accepted within industry.

3	Legislation and publications relevant to this unit standard include:

Health and Safety in Employment Act 1992 and Health and Safety in Employment Regulations 1995;

Building Act 2004;

Resource Management Act 1991;

AS 3958.1:2007, Ceramic tiles - Guide to the installation of ceramic tiles; available from https://www.saiglobal.com/pdftemp/previews/osh/as/as3000/3900/3958.1-2007.pdf.

Outcomes and performance criteria

Outcome 1

Demonstrate knowledge of tile installation.

Range	floor, wall; one installation must be for a wet area.

Performance criteria

1.1	Installation requirements are explained in terms of job requirements and work site practice.

Range	set-up of work area, surface preparation, primers and adhesives, grouts, sealers, flexible sealants.

1.2	Quantities of tiles and other materials are calculated to meet job requirements.

1.3	Tile set-out requirements are explained in terms of job requirements and work site practice.

1.4	Tile layout procedures are explained in terms of job requirements and work site practice.

Range	pattern, design.

1.5	Tile installation procedures are explained in terms of job requirements and work site practice.

1.6	Tile cutting methods and techniques are explained in terms of work site practice.

Range	wet, dry;

mechanical, manual.

Outcome 2

Cut tiles on site.

Range	manual cutting – dry;

mechanical cutting – wet and dry.

Performance criteria

2.1	Cuts and cutting methods are determined as indicated by the set-out, and to meet tile type and manufacturer’s specifications.

2.2	Tiles are cut in accordance with job specifications and work site practice.

Outcome 3

Install floor and wall tiles on site.

Range	two floors, two walls;

one installation must be for a wet area;

floors must include one level and one fall.

Performance criteria

  - Tiles are laid and spaced in accordance with job specifications and work site practice.

  - Completed job is in accordance with job specifications.

Outcome 4

Complete work operations.

Performance criteria

4.1	All operations are safely completed; workplace, tools, plant and equipment are cleaned; and tools, plant and equipment are stored in accordance with work site practice.

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 16 December 2005 | 31 December 2024 |
| Review | 2 | 18 February 2011 | 31 December 2024 |
| Review | 3 | 30 June 2022 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0048 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.