| Title | Apply finishing coats to prepared Proprietary Plaster Cladding substrates on site |
| --- | --- |
| Level | 4 | Credits | 20 |

| Purpose | People credited with this unit standard are able to: identify required surface finish from job or contract specifications; prepare levelled surfaces for the application of finish coats; mix and condition finishing compound; apply finish coat compound to a prepared background; apply final coat to the system; and complete work operations on site. |
| --- | --- |

| Classification | Construction Trades > Proprietary Plaster Cladding Systems |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Definitions

On site refers to a wide range of building and construction environments within which the Proprietary Plaster Cladding Systems trade skills are applied.

Plant is used as in the Health and Safety in Employment Act 1992 to mean appliances, equipment, fittings, furniture, implements, machines, machinery, tools, vehicles, plus parts, controls, and anything connected.

Specifications refers to documented instructions (oral, written, graphic) and may include any of the following:  manufacturer’s specifications, recommendations or technical data sheets; material specifications; specifications from a specialist source such as an architect, designer, engineer or a supervisor; site or work specific requirements.

Work site practice refers to the documented procedures specific to a work site, which set out the standard and required practices of that work site.

2	Legislation, regulations, codes and standards relevant to this unit standard include:

Health and Safety in Employment Act 1992;

Health and Safety in Employment Regulations 1995;

Resource Management Act 1991;

Hazardous Substances and New Organisms Act 1996; Building Act 2004;

New Zealand Standards, NZS 4218:2004 Energy efficiency – Small building envelope and NZS 3604:1999 Timber Framed Buildings, available from Standards NZ (http://www.standards.co.nz);

New Zealand Building Code;

Territorial Authorities’ building regulations.

3	Credit for this unit standard indicates compliance with industry practice.  Industry practice refers to the ability to demonstrate knowledge and skills that reflect the productivity, uniformity, finish quality and material economies currently accepted within industry.

Outcomes and performance criteria

Outcome 1

Identify required surface finish from job or contract specifications.

Performance criteria

1.1	Compatibility of the surface with specified proprietary finishing compound is checked.

1.2	The intended finish coat application is checked against job specifications.

Range	four of – colour, texture, thickness, durability, maintainability, specified product.

Outcome 2

Prepare levelled surfaces for the application of finish coats.

Performance criteria

2.1	Surfaces are checked for any defects and identified defects are rectified.

Range	two of – damaged, delaminated, out of level.

2.2	Surface sealing procedures are actioned if required, before finishing coat applications, to meet job specifications.

Range	solvent or emulsion.

Outcome 3

Mix and condition finishing compound.

Performance criteria

3.1	The measuring and mixing of selected finishing compounds are described and completed in accordance with the manufacturer’s instructions and job specifications.

Range	four of – weights, volumes, drill mixers, proprietary additives, viscosity, texture type, personal protection.

3.2	The storage and care of mixed finishing compounds are described in accordance with the manufacturer’s instructions.

Range	pot life, retempering, temperature.

Outcome 4

Apply finish coat compound to a prepared background.

Performance criteria

4.1	The finishing plaster materials are applied to prepared backgrounds using suitable tools.

Range	application tools include three of – roller, brush, sponge, trowels, broadknives, hopper guns, spray guns.

4.2	The finishing plaster is finished according to specifications.

Range	three of – spray texture, sponge, trowel, drag, undulating.

4.3	Curing requirements for finishing plasters are determined in accordance with the material used, time of application, manufacturer’s instructions, and working conditions.

Range	finish effect, final coating system, manufacturer’s instructions, weather conditions, time restrictions, environmental conditions.

Outcome 5

Apply final coat to the system.

Performance criteria

5.1	The final coat is selected for the system.

Range	three of – paint, highbuild, glaze, elastomeric, cement wash, lime wash.

5.2	The final coat is applied according to job specifications and client choice, using suitable tools.

Range	tools include two of – paint brush, roller, airless spray, spray gun, hopper gun.

5.3	Curing requirements for finishing coat membranes are determined in accordance with job specifications.

Range	three of – finish effect, manufacturer’s instructions, weather conditions, time restrictions, environmental conditions.

Outcome 6

Complete work operations on site.

Performance criteria

6.1	All operations are completed without damage to project, plant and materials.

6.2	All operations comply with the requirements of the site safety plan.

6.3	All plant is used, maintained, repaired, cleaned, and stored in accordance with manufacturer’s specifications and work site practice.

6.4	Surplus and waste materials are dealt with in accordance with work site practice and site is left as specified in the terms of the contract.

| Replacement information | This unit standard replaced unit standard 17512. |
| --- | --- |

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 24 January 2006 | 31 December 2024 |
| Review | 2 | 26 January 2007 | 31 December 2024 |
| Review | 3 | 30 June 2022 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0048 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.