| Title | Demonstrate knowledge of installation methods in the flooring industry |
| --- | --- |
| Level | 2 | Credits | 4 |

| Purpose | This unit standard is for people entering the flooring industry. People credited with this unit standard are able to demonstrate knowledge of installation methods in the flooring industry. |
| --- | --- |

| Classification | Construction Trades > Flooring |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

Definition

Workplace procedures are all authorised instructions, processes and work practices carried out in the workshop, factory, shop and worksite.

Outcomes and performance criteria

Outcome 1

Demonstrate knowledge of installation methods in the flooring industry.

Performance criteria

1.1	Methods used to install cork flooring products are identified and described in terms of techniques used, and materials and equipment required for the job.

Range	methods include but are not limited to – mono-bond, water based or neoprene adhesive, tile installation, cork sheet installation.

1.2	Methods used to install carpet by conventional and adhesive methods are identified and described in terms of techniques used, and materials and equipment required for the job.

Range	methods include but are not limited to – joining, edge fixings, stair applications, stretching techniques, trimming, coving, single/double bond.

1.3	Methods used to install laminated and solid timber flooring overlays are identified and described in terms of techniques used, and materials and equipment required for the job.

Range	methods include but are not limited to – floating, direct stick, through surface fixed or secret nail installation.

1.4	Methods used to install resilient sheet and tile floorcoverings are identified and described in terms of techniques used, and materials and equipment required for the job.

Range	methods include but are not limited to – template, bar-scribe, freehand and stepping cutting techniques, coving, wallcladding, stairs/stringers, nosings, thermoplastic welding.

1.5	Methods used to install resilient sheet for wet areas are identified and described in terms of techniques used, and materials and equipment required for the job.

Range	methods include but are not limited to – template, bar-scribe, freehand and stepping cutting techniques, coving, wallcladding, stairs/stringers, nosings, thermoplastic welding, waste and protrusion sealing, substrate gradients, moisture egress protection.

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 26 March 2007 | 31 March 2017 |
| Review | 2 | 18 February 2011 | 31 December 2024 |
| Review | 3 | 25 November 2021 | 31 December 2024 |
| Rollover | 4 | 30 November 2023 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0175 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.