| Title | Proof load lifting equipment components, and certify for use |
| --- | --- |
| Level | 5 | Credits | 15 |

| Purpose | People credited with this unit standard are able to: proof load lifting equipment components, and proof load and visually examine complete assemblies; and record information from proof loading and visual inspection, and certify lifting equipment components for use. This unit standard is for people involved with inspection and certification of lifting equipment. |
| --- | --- |

| Classification | Lifting Equipment > Rigging |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

| Prerequisites | Unit 23448, Carry out safety checks of lifting equipment components, and certify for use, or demonstrate equivalent knowledge and skills. |
| --- | --- |

Guidance Information

1	Legislation relevant to this unit standard includes but is not limited to the Health and Safety in Employment Act 1992.

2	Definition

Lifting equipment components – slings, shackles, fittings, pulley blocks.

3	Assessment

Evidence is required for:

slings – chain, wire rope, web, round;

shackles – standard, high capacity;

fittings – eyebolts, rigging screws, turnbuckles;

pulley blocks – single sheave, multiple sheave.

4	Lifting equipment components must be inspected for wear and damage, and certified to the standards specified in unit standard 23448 prior to proof loading.

5	International Accreditation New Zealand (IANZ) requirements are available from http://www.ianz.govt.nz.

6	Working Load Limit (WLL) specifications are found in the standards listed in manufacturer’s specifications.

7	Manufacturer’s specifications are based on internationally recognised standards which include but are not limited to –

Web Slings

AS 1353: 1997, Flat synthetic-webbing slings – Product specification, Part 1.

BS EN 1492: 2004, Textile slings – Safety – Lifting slings for general service made from certain natural and man-made fibre ropes, Part 1.

BS EN 1492: 2004, Textile slings – Safety – Lifting slings for general service made from natural and man-made fibre ropes, Part 4.

Round Slings

AS 4497: 1997, Round slings – Synthetic fibre – Product specifications, Part 1.

BS EN 1492: 2004, Textile slings – Safety – Lifting slings for general service made from natural and man-made fibre ropes, Part 2.

Chain Slings

AS 2321.2001 Short-link chain for lifting purposes.

AS 3776: 2006, Lifting components for Grade T chain slings.

BS EN 818: 1996-2000, Short link chain for lifting purposes – Safety, Parts 1-6.

BS EN 1677: 2000, Components for slings – Safety, Parts 1 and 2.

ISO 4778:1981, Chain slings of welded construction – Grades M(4), S(6), and T(8).

ISO 7593: 1986, Chain slings assembled by methods other than welding – Grade T(8).

JIS B 8816: 2004, Chain slings for lifting purposes.

Shackles

AS 2741: 2002, Shackles.

Federal Specifications RC-C-271D: 1990, Chains and attachments, welded and weldless.

Eyebolts and Nuts

BS 4278: 1984, Specifications for eyebolts for lifting purposes.

DIN 580: 2003-08, Eye Bolts.

DIN 582: 2003-08, Eye Nuts.

Rigging Screws and Turnbuckles

BS 4429: 1987, Specification for rigging screws and turnbuckles for general engineering, lifting purposes, and pipe hanger applications.

Pulley Blocks

BS MA 47: 1977, Code of Practice for ship’s cargo blocks.

Wire Rope Slings

BS EN 13414: 2003, Steel wire rope slings – Safety, Parts 1-3.

Australian Standards (AS) are available from http://www.standards.com.au/.

Japanese Standards (JIS) are available from http://www.jsa.or.jp/.

ISO Standards are available from http://www.iso.org/.

CEN/EN Standards are available from https://www.cencenelec.eu/.

British Standards (BS) are available from https://www.bsigroup.com/.

German Standards (DIN) are available from https://www.din.de/en.

8	Lifting Equipment Engineers of New Zealand (LEENZ) requirements and Code of Practice for the Safe Use of Lifting Equipment (referred to as the code of practice), are available from LEENZ Inc, PO Box 13015, Onehunga, Auckland.

9	Reference

OSH Approved Code of Practice for Load-Lifting Rigging, available from the Occupational Safety and Health Service of the Department of Labour website, https://www.worksafe.govt.nz/.

Outcomes and performance criteria

Outcome 1

Proof load lifting equipment components, and proof load and visually examine complete assemblies.

Performance criteria

1.1	Test bed for proof loading is calibrated in accordance with International Accreditation New Zealand (IANZ) requirements.

1.2	Lifting equipment components are proof loaded on test bed in accordance with manufacturer’s specifications.

1.3	Lifting equipment components are proof loaded in accordance with WLL specifications.

1.4	Complete assemblies are visually examined for damage, permanent stretch, or deformation in accordance with manufacturer’s specifications.

Outcome 2

Record information from proof loading and visual inspection, and certify lifting equipment components for use.

Performance criteria

2.1	Information from proof loading and visual inspection is recorded in accordance with LEENZ requirements.

  - Proof load certification is completed in accordance with LEENZ requirements.

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 23 February 2007 | 31 December 2024 |
| Review | 2 | 27 October 2022 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0025 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.