| Title | Demonstrate knowledge of alterations and additions for construction |
| --- | --- |
| Level | 4 | Credits | 3 |

| Purpose | People credited with this unit standard are able to describe: requirements of an on site pre construction investigation; the construction process when making an alteration or addition at the same or a split level; raising an existing building and adding a bottom storey; the methods of adding a top storey to an existing building; excavating under an existing building to form a new basement; the construction of timber decks; and procedures for maintaining health and safety requirements when constructing alterations and additions on site. |
| --- | --- |

| Classification | Construction Trades > Carpentry Theory |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Definition

Specific design is a design that ensures compliance with the Building Act 2004 when the construction requirements of a building deviates from, or is beyond the scope of recognised industry standards (New Zealand Standards, Australia/New Zealand Standards, British Standards and other published standards that govern the construction industry).

2	Credit for this unit standard indicates compliance with industry practice.  Industry practice refers to the ability to demonstrate knowledge that reflects the uniformity, finish quality and material economies currently accepted within industry.

3	Legislation relevant to this unit standard includes:

Health and Safety in Employment Act 1992 and Health and Safety in Employment Regulations 1995;

Building Act 2004;

Building Regulations 1992 and Building (Forms) Regulations 2004;

Resource Management Act 1991;

New Zealand Building Code;

NZS 3604:1999 Timber Framed Buildings, available from Standards NZ (http://www.standards.co.nz).

Outcomes and performance criteria

Outcome 1

Describe requirements of an on site pre-construction investigation.

Performance criteria

1.1	Information requirements for an on site pre-construction investigation are described.

Range	clear space available; slope of the ground; bearing capacity of the ground; position of services; area taken up by drives and paths; existing trees and other items to be retained; position, area and details of existing buildings; hazardous materials; insurance responsibilities, occupancy.

1.2	The use of on site pre-construction investigation data, in conjunction with design documents, is described in terms of determining the construction process.

Outcome 2

Describe the construction process when making an alteration or addition at the same or a split level.

Performance criteria

2.1	Methods are described for opening up existing buildings and joining up to match.

2.2	Options for temporary weather protection are described in terms of job requirements.

2.3	Methods used to maintain existing services are described in terms of minimum disruption.

Range	electricity, gas, communications systems, water, stormwater, sewerage.

Outcome 3

Describe raising an existing building and adding a bottom storey.

Performance criteria

3.1	Preparatory work for raising a building is described.

3.2	Methods of raising and supporting an existing building are described.

3.3	Excavation and construction are described in terms of adding a bottom storey to an existing building.

3.4	Final work is described in terms of adding a bottom storey.

Range	lowering, fixing, ‘making good’.

Outcome 4

Describe the methods of adding a top storey to an existing building.

Performance criteria

4.1	Methods of strengthening an existing building are described in terms of adding a new top storey.

4.2	Location, construction and installation of access stairs are described in accordance with the requirements of the Building Code.

4.3	Methods of construction and temporary weatherproofing are described in terms of adding a new top storey to an existing building.

Outcome 5

Describe excavating under an existing building to form a new basement.

Performance criteria

5.1	The methods of excavation and temporary support of an existing building are described in terms of excavating under it.

5.2	Installation of beams, beam supports and retaining walls is described in terms of forming a new bottom storey under an existing building.

5.3	Construction of a bottom storey and access stairs is described in terms of adding a bottom storey under an existing building.

Outcome 6

Describe the construction of timber decks.

Performance criteria

6.1	Functions of members of a timber deck are described.

Range	piles, post, bearers, beams, joist, bracing, decking, balustrades, mechanical fixings.

6.2	Construction requirements of decks are described.

Range	NZS 3604:1999 or specific design.

Outcome 7

Describe procedures for maintaining health and safety requirements when constructing alterations and additions on site.

Performance criteria

7.1	Procedures for maintaining health and safety requirements when constructing alterations and additions are described.

Range	work methods, plant, equipment, identification of hazards and controls.

| Replacement information | This unit standard replaced unit standard 13030. |
| --- | --- |

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 25 January 2008 | 31 December 2023 |
| Review | 2 | 30 September 2021 | 31 December 2023 |
| Rollover | 3 | 28 September 2023 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0048 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.