| Title | Demonstrate knowledge of brix measurement procedures and take brix samples |
| --- | --- |
| Level | 2 | Credits | 2 |

| Purpose | People credited with this unit standard are able to: demonstrate knowledge of brix measurement procedures; and take brix samples. |
| --- | --- |

| Classification | Food and Related Products Processing > Food and Related Product Production |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Legislation relevant to this unit standard may include but is not limited to:
Health and Safety at Work Act 2015.
Food Act 2014.
Food Regulations 2015.
Resource Management Act 1991.

2	Definitions

Organisational procedures refer to documents that include: worksite rules, codes, and practices; equipment operating instructions; manufacturer’s specifications; production specifications; documented quality management systems; and health and safety requirements, including the use of PPE.

PPE refers to personal protective equipment such as protective clothing, gloves, safety glasses, headwear, footwear, hearing protection, safety devices.

3	Assessment information

All activities and evidence must be in accordance with organisational procedures.

Outcomes and performance criteria

Outcome 1

Demonstrate knowledge of brix measurement procedures.

Performance criteria

1.1	The meaning of the term brix is described.

Range	refining process – process flows, finished products.

1.2	The methods for measuring brix are described.

Range	equipment – laboratory refractometer, hand-held refractometer, spindle hydrometer.

1.3	Reasons for possible deviations from expected brix values are explained.

Range	deviations include but are not limited to – instrument calibration, temperature.

1.4	The impact of deviations from expected brix values to the process are explained.

Outcome 2

Take brix samples.

Performance criteria

2.1	Brix sampling equipment is handled in a manner which avoids contamination in accordance with manufacturer’s specification.

2.2	Brix sampling equipment is checked for function, and faults are identified and repaired or reported.

2.3	Brix samples are taken in accordance with laboratory protocol, recorded, and labelled.

Range	includes but is not limited to – micro-sampling, process sampling, finished product sampling.

| Planned review date | 31 December 2025 |
| --- | --- |

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 27 February 2008 | 31 December 2022 |
| Review | 2 | 25 February 2021 | N/A |

| Consent and Moderation Requirements (CMR) reference | 0013 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.

Comments on this unit standard

Please contact Competenz qualifications@competenz.org.nz if you wish to suggest changes to the content of this unit standard.