| Title | Install flashings for metal roof tiles |
| --- | --- |
| Level | 4 | Credits | 15 |

| Purpose | This unit standard is intended for use in the training and assessment of people carrying out metal tile roof work and covers the installation of flashings for metal tile roofs. People credited with this unit standard are able to install flashings for metal roof tiles. |
| --- | --- |

| Classification | Plumbing, Gasfitting and Drainlaying > Roofing |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	This unit standard has been developed for learning and assessment on-job.

2	References

Construction Contracts Act 2002;

Historic Places Act 1993;

Local Government Act 2002;

Building Act 2004 and associated regulations;

Health and Safety at Work Act 2015;

Resource Management Act 1991;

Acceptable Solutions and Verification Methods for New Zealand Building Code Clause E2 External Moisture;

Licensed Building Practitioner Scheme – Understanding the Regulatory Environment Booklet – available at: http://www.business.govt.nz/lbp/the-board/getting-licensed/applying-for-licensing;

NZS 3604:2011 Timber-framed buildings;

NZS 3902:2004 Housing, alterations and small buildings contract;

NZS 4121:2001, Design for access and mobility: Buildings and associated facilities;

New Zealand Building Code Hand Book – available at: http://www.building.govt.nz/building-code-compliance/building-code-and-handbooks/building-code-handbook;

and all subsequent amendments and replacements.

3	This unit standard applies to both new roof and re-roofing installations.

4	Range

a	Candidates must refer to current legislation and Standards during assessment.

b	Demonstration of safe working practices are essential components of assessment of this unit standard.

c	All activities and evidence presented for all outcomes and performance criteria in this unit standard must be in accordance with:

i	legislation;

ii	policies and procedures;

iii	ethical codes;

iv	Standards – may include but are not limited to those cited in the New Zealand Building Code Hand Book;

v	applicable site, enterprise, and industry practice; and,

vi	manufacturers’ instructions, specifications, and data sheets.

Outcomes and performance criteria

Outcome 1

Install flashings for metal roof tiles.

Performance criteria

1.1	Identify flashing requirements from plan and specifications.

1.2	Install flashings in accordance with job specifications.

Range	wall flashings, penetration flashings, back gutter.

1.3	Correct any defects.

1.4	Remove surplus material including swarf and leave roof and site in a tidy and safe condition that allows any further work to be carried out safely.

| Planned review date | 31 December 2023 |
| --- | --- |

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 23 January 2009 | 31 December 2020 |
| Review | 2 | 16 March 2017 | N/A |
| Rollover | 3 | 25 August 2022 | N/A |

| Consent and Moderation Requirements (CMR) reference | 0003 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.

Comments on this unit standard

Please contact the Waihanga Ara Rau Construction and Infrastructure Workforce Development Council qualifications@waihangaararau.nz if you wish to suggest changes to the content of this unit standard.