| Title | Demonstrate knowledge of processing toughened and heat strengthened glass |
| --- | --- |
| Level | 4 | Credits | 5 |

| Purpose | This theory-based unit standard is for experienced people in the glass processing industry working with specialist glass. People credited with this unit standard are able to describe compliance requirements applying to manufacturing toughened and heat strengthened glass; describe preparation to manufacture toughened and heat strengthened glass; and demonstrate knowledge of horizontal glass tempering machines used to manufacture toughened and heat strengthened glass. |
| --- | --- |

| Classification | Glass and Glazing > Glass Processing and Manufacturing |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Definitions

Compliance requirements – refer to those New Zealand Standards, Australia/New Zealand Standards, and tests which apply to the processing of toughened and heat strengthened glass.

Worksite requirements – refer to instructions to staff on policy and procedures which are documented in memo or manual format and are available in the workplace.  These requirements include – company specifications and procedures, work instructions, manufacturer’s specifications, product quality specifications, legislative requirements.

2	Legislation and standards relevant to this unit standard include – Health and Safety at Work Act 2015, Resource Management Act 1991 and the following Australia/New Zealand Standards:

AS/NZS 2208:1996 Safety glazing materials in buildings

AS/NZS 2080:2006 Safety glazing for land vehicles, available at http://www.standards.co.nz.

3	Range

Types of glass which can be toughened or heat strengthened by the processes covered in this unit standard are limited to – float glass from 4 mm to 19 mm in thickness, obscure glass with shallow patterns.

Outcomes and performance criteria

Outcome 1

Describe compliance requirements applying to manufacturing toughened and heat strengthened glass.

Performance criteria

1.1	Purposes and compliance requirements for manufacturing toughened and heat strengthened glass are described.

1.2	Scope and focus of standards applying to manufacturing toughened and heat strengthened glass are described.

Range	standards include – AS/NZS 2208:1996, AS/NZS 2080:2006

1.3	Focus and purpose of tests applied in manufacturing toughened and heat strengthened glass are described in terms of worksite requirements.

Range	tests include – size test, thickness test, squareness test, uniformity test, heat shock test, load stamp test, fragmentation test, light transmission test, bow test, edge inspection, parallelism test, flatness test, impact test.

Outcome 2

Describe preparation to manufacture toughened and heat strengthened glass.

Performance criteria

2.1	Requirements for preparing the work area and personal safety precautions are described in terms of worksite requirements.

Range	preparation includes – selection and use of protective clothing and safety equipment, checks of emergency stops and battery drives on machine, identification of hazards, review of operational procedures, clearing work area.

2.2	Process for checking glass to be manufactured is described in terms of worksite requirements.

Range	checks include – glass and processing system to be used match with requirements of work and/or customer order; completion of relevant standards tests; glass size is within processing equipment limitations; glass manufacturer’s size and processing limitations; printing face, shapes and patterns for printing table placement.

2.3	Process for preparing to manufacture toughened or heat strengthened glass is described in terms of worksite requirements.

Range	process includes – marking of glass with standards identification in accordance with works instruction, selection and positioning of glass on loading table, inputting of machine settings for type of glass being toughened.

Outcome 3

Demonstrate knowledge of horizontal glass tempering machines used to manufacture toughened and heat strengthened glass.

Performance criteria

3.1	Process for pre-start, start and set-up procedures is described in terms of worksite requirements.

3.2	Procedures for forwarding glass into the furnace are identified and described in terms of worksite requirements.

3.3	Process for monitoring and adjusting the furnace operation is described in terms of worksite requirements.

3.4	Emergency procedures if glass breakage occurs in the furnace are described in terms of worksite requirements.

| Planned review date | 31 December 2022 |
| --- | --- |

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 21 May 2010 | 31 December 2017 |
| Review | 2 | 18 June 2015 | N/A |
| Rollover and Revision | 3 | 25 August 2022 | N/A |

| Consent and Moderation Requirements (CMR) reference | 0073 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.

Comments on this unit standard

Please contact Hanga-Aro-Rau Manufacturing, Engineering and Logistics Workforce Development Council at qualifications@hangaarorau.nz if you wish to suggest changes to the content of this unit standard.