| Title | Demonstrate knowledge, and carry out curing, of concrete |
| --- | --- |
| Level | 2 | Credits | 8 |

| Purpose | People credited with this unit standard are able to: demonstrate knowledge of curing concrete; carry out curing of concrete; and complete work operations. |
| --- | --- |

| Classification | Concrete > Concrete Core Skills |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Definitions

Specifications refer to documented instructions (oral, written, graphic) and may include any of the following: manufacturer’s specifications, recommendations or technical data sheets; material specifications; specifications from a specialist source such as an architect, designer, engineer or a supervisor; site or work specific requirements.

Workplace practice refers to the documented procedures specific to a workplace which set out the standard and required practices of that workplace.

2	Legislation and publications relevant to this unit standard include:

Health and Safety in Employment Act 1992 and Health and Safety in Employment Regulations 1995;

Resource Management Act 1991;

NZS 3109:1997 Concrete construction, available from Standards New Zealand (http://www.standards.co.nz).

Outcomes and performance criteria

Outcome 1

Demonstrate knowledge of curing concrete.

Performance criteria

1.1	Curing of concrete is defined and explained in terms of process.

1.2	Factors affecting curing of concrete are described in terms of their effect on the strength and durability of the finished product.

Range	rate of moisture loss, temperature, mix design, rate of curing.

1.3	Methods to control curing of concrete are described, and considerations when selecting a curing method are explained in terms of end use of the finished product.

Range	four of – applied membrane, water, sheet membrane, steam, admixtures, applied heat, controlled environment.

Outcome 2

Carry out curing of concrete.

Range	two of – applied membrane, water, sheet membrane, steam, admixtures, applied heat, controlled environment, proprietary spray.

Performance criteria

2.1	Conditions required for curing are met in accordance with job specifications and NZS 3109.

Range	moisture, temperature.

2.2	Curing period is identified and monitored in accordance with specifications and workplace practice.

2.3	Actions taken to correct any faults during curing are in accordance with specifications and workplace practice.

2.4	Curing is completed in accordance with workplace practice.

Outcome 3

Complete work operations.

Performance criteria

3.1	All operations are safely completed, workplace and equipment are cleaned in accordance with workplace practice and environmental safety requirements, and routine maintenance is carried out in accordance with workplace practice.

| Replacement information | This unit standard replaced unit standard 12033. |
| --- | --- |

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 20 November 2009 | 31 December 2024 |
| Review | 2 | 24 November 2022 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0048 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.