| Title | Demonstrate knowledge of defects and carry out remedial work on concrete |
| --- | --- |
| Level | 3 | Credits | 15 |

| Purpose | People credited with this unit standard are able to: demonstrate knowledge of defects in concrete; carry out remedial work to remedy defects in concrete; and complete work operations. |
| --- | --- |

| Classification | Concrete > Concrete Core Skills |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Definitions

Specifications refer to documented instructions (oral, written, graphic) and may include any of the following: manufacturer’s specifications, recommendations or technical data sheets; material specifications; specifications from a specialist source such as an architect, designer, engineer or a supervisor; site or work specific requirements.

Workplace practice refers to the documented procedures specific to a workplace which set out the standard and required practices of that workplace.

2	Credit for this unit standard indicates compliance with industry practice.  Industry practice refers to the ability to demonstrate knowledge and skills that reflect the productivity, uniformity, finish quality, and material economies currently accepted within industry.

3	Legislation and publications relevant to this unit standard include:

Health and Safety in Employment Act 1992 and Health and Safety in Employment Regulations 1995;

3109:1997 Concrete construction and NZS 3114:1987 Specification for concrete surface finishes, available from Standards New Zealand (http://www.standards.co.nz).

Outcomes and performance criteria

Outcome 1

Demonstrate knowledge of defects in concrete.

Range	surface defects, four of – fins, ledges, plastic cracks up to 12mm deep, blowholes, tie holes, colour, grout loss, uncompacted concrete, physical damage, delamination, dominant joints, damaged saw cuts, flatness and levelness outside of tolerances, boniness/honeycombing, chips, steps in seams, edging, bulges;

structural defects, four of – cracks, incorrect fixing positions, major grout loss, incorrect reinforcing cover, concrete thickness, broken or chipped concrete, incorrect penetrations/lifting system installation, incorrect overall dimensions, foreign objects.

Performance criteria

1.1	Structural and surface defects are identified and described in accordance with NZS 3109, NZS 3114, or specifications.

1.2	Causes and implications of structural and surface defects in concrete are identified.

1.3	Methods for eradication, minimisation or rectification of structural and surface defects in concrete are identified and described in accordance with NZS 3109, NZS 3114, specifications, and workplace practice.

Outcome 2

Carry out remedial work to remedy defects in concrete.

Performance criteria

2.1	Remedial work is completed to remedy surface defects in accordance with job specifications, NZS 3109, NZS 3114, and workplace practice.

Range	four of – fins, ledges, plastic cracks up to 12mm deep, blowholes, tie holes, colour, grout loss, uncompacted concrete, physical damage, delamination, dominant joints, damaged saw cuts, flatness and levelness outside of tolerances, boniness/honeycombing, chips, steps in seams, edging, bulges.

2.2	Actions taken to remedy structural defects are in accordance with job specifications, NZS 3109, NZS 3114, and workplace practice.

Range	four of – cracks, incorrect fixing positions, major grout loss, incorrect reinforcing cover, concrete thickness, broken or chipped concrete, incorrect penetrations/lifting system installation, incorrect overall dimensions, foreign objects.

Outcome 3

Complete work operations.

Performance criteria

3.1	All operations are safely completed, workplace and equipment are cleaned in accordance with workplace practice and environmental safety requirements, and routine maintenance is carried out in accordance with workplace practice.

3.2	Any required documentation is completed in accordance with workplace practice.

| Replacement information | This unit standard replaced unit standard 12034. |
| --- | --- |

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 20 November 2009 | 31 December 2024 |
| Review | 2 | 24 November 2022 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0048 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.