| Title | Determine and describe construction of small buildings |
| --- | --- |
| Level | 5 | Credits | 20 |

| Purpose | People credited with this unit standard are able to, for a small building, determine and describe: the foundations and substructure; the structure, the envelope, and the interior. |
| --- | --- |

| Classification | Construction > Core Planning and Construction |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Definitions

Alternative construction materials are materials other than those traditionally used for building, such as rammed earth, cob, straw bale, mud brick, and/or polystyrene blocks.

Design requirements refer to requirements for sustainability, durability, appearance, maintenance, practicality for intended use, general cost implications and water/weathertightness.

Small buildings are small scale, light weight buildings, generally of non-specific design, and of domestic scale with lightweight framing and/or concrete or concrete masonry construction.

Buildability refers to – ease of construction, availability of plant, equipment and materials, site access, and construction sequence.

2	It is expected that the candidate will demonstrate an understanding of the concept of buildability.

3	Evidence should include sketching whenever possible.

4	Assessment of this unit standard can be by simulation using given site information, and/or observation.

5	Legislation and publications relevant to this unit standard include: Health and Safety in Employment Act 1992 and Health and Safety in Employment Regulations 1995;

Resource Management Act 1991;

Building Act 2004;

New Zealand Building Code;

NZS 3604:1999 Timber framed buildings, and NZS 4229:1999 Concrete masonry buildings not requiring specific engineering design, available from Standards New Zealand (http://www.standards.co.nz).

6	It is recommended that the outcomes of this unit standard be achieved in conjunction with Unit 9663, Demonstrate knowledge of a research/feasibility study of a site.

Outcomes and performance criteria

Outcome 1

Determine and describe the foundations and substructure for a small building.

Performance criteria

1.1	Description addresses geotechnical factors.

1.2	Description is in accordance with building use and design requirements.

1.3	Construction process is explained in terms of site constraints, materials, and time and general cost implications.

Range	materials – timber, concrete, steel.

Outcome 2

Determine and describe the structure of a small building of non-specific design.

Performance criteria

2.1	Description includes provision for services, materials, cladding and finishes.

2.2	Description is in accordance with building use and design requirements.

2.3	Construction process is explained in terms of site constraints, materials, and time and general cost implications.

Range	materials – timber, in-situ reinforced concrete, concrete masonry blockwork.

Outcome 3

Determine and describe the structure of a small building of specific design.

Performance criteria

3.1	Description includes provision for services, materials, cladding and finishes.

3.2	Description is in accordance with building use and design requirements.

3.3	Construction process is explained in terms of site constraints, materials, and time and general cost implications.

Range	materials – timber, structural steel, reinforced concrete, steel stud, concrete masonry blockwork, any alternative construction materials.

Outcome 4

Determine and describe the envelope of a small building.

Performance criteria

4.1	Selection and design for wall and roof claddings and openings matches the characteristics of the required structure.

Range	materials, four of – timber, rendering, metal sheet, cellulose cement, masonry, concrete, glass.

4.2	Design principles of typical cladding jointing systems are described in terms of sealants, flashings, and compatibility and jointing between systems.

4.3	Description includes provision for services, materials, and finishes.

4.4	Description is in accordance with building use and design requirements.

4.5	Construction process is explained in terms of site constraints, materials, and time and general cost implications.

Range	materials, four of – timber, rendering, metal sheet, cellulose cement, masonry, concrete, glass.

Outcome 5

Determine and describe the interior of a small building.

Range	linings, joinery, fitments.

Performance criteria

5.1	Selection of the interior matches the characteristics of the required structure.

5.2	Description matches or exceeds the regulatory requirements that apply to the approved solutions.

5.3	Description includes provision for services, materials, and finishes.

5.4	Construction process is explained in terms of site constraints, materials, and time and general cost implications.

| Replacement information | This unit standard replaced unit standard 9671. |
| --- | --- |

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 18 March 2011 | 31 December 2024 |
| Review | 2 | 25 August 2022 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0048 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.