| Title | Describe the procedures and process and complete a set-out for the manufacture of timber geometric stairs |
| --- | --- |
| Level | 4 | Credits | 20 |

| Purpose | People credited with this unit standard are able to: describe the preparation procedures; describe the process; and complete a half-sized set-out for the manufacture of timber geometric stairs. |
| --- | --- |

| Classification | Joinery > Joinery Operational Skills |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Legislation and standards relevant to this unit standard include:

- Health and Safety at Work Act 2015; available from www.legislation.govt.nz;

- NZS 3610:1979; Specification for profiles of mouldings and joinery, available from www.standards.co.nz, and any subsequent amendments and replacements.

2	Assessment

Evidence for this unit standard must reflect commercial competence; the ability to demonstrate knowledge and skills in the context of the currently accepted requirements of a business operating in a commercial environment.

Evidence must also reflect commercial standards; the verbal and written information covering company policy, standard operating procedures and processes and job-specific instructions.

This unit standard must be assessed under the supervision of a commercially competent practitioner in workplace conditions that reflect:

- commercial standards, current health, safety, industry, and workplace requirements; and

- industry requirements for commercially acceptable timeframes.

3	Definitions

Geometric stairs refer to continuous stairs that turn or wind about a central wellhole that has rounded corners or is circular or elliptical and that have the strings and rails arranged upon geometric principles and running continuously from top to bottom.

Workplace requirements refer to the documented procedures specific to a workplace which set out the standard and the required practices of that workplace. This may include job specifications, procedures, practices, manufacturer recommendations, technical data sheets and material safety data sheets.

Outcomes and performance criteria

Outcome 1

Describe the preparation procedures for the manufacture of timber geometric stairs.

Performance criteria

1.1	Working drawings are described in terms of the information they provide, and the type of stair required for the job.

1.2	The importance of the site visit is described in terms of the measurements and preparation of the work area.

1.3	The procedures for set out are described in accordance with the job specifications.

1.4	Procedures for preparation of the cutting list are described.

Outcome 2

Describe the process for the manufacture of timber geometric timber stairs.

Performance criteria

2.1	The set out procedures are described in terms of the set out on full-sized formers according to the working drawings.

2.2	The manufacturing procedures are described in terms of the manufacturing process and how it meets the job specifications.

Range	stair timber machined to match the set-out, working the joints, laminations glued for curved components, assembling, trimming, installation.

2.3	The procedures for handrails and balustrades is described in terms of assembling, trimming, fitting and fixing.

2.4	The finishing and protecting procedures are described in terms of the job specification.

2.5	Post-operational procedures are described in accordance with workplace requirements.

Outcome 3

Complete a half-sized set-out for the manufacture of timber geometric stairs.

Performance criteria

3.1	Working drawings for half-sized set-out for geometric stairs are completed in accordance with the job specifications.

| Replacement information | This unit standard replaced unit standard 2533 and unit standard 25605. |
| --- | --- |

| Planned review date | 31 December 2027 |
| --- | --- |

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 24 October 2014 | 31 December 2025 |
| Review | 2 | 30 March 2023 | N/A |

| Consent and Moderation Requirements (CMR) reference | 0073 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.

Comments on this unit standard

Please contact Waihanga Ara Rau Construction and Infrastructure Workforce Development Council at qualifications@WaihangaAraRau.nz if you wish to suggest changes to the content of this unit standard.