| Title | Demonstrate knowledge of routing and switching essentials in power engineering |
| --- | --- |
| Level | 5 | Credits | 15 |

| Purpose | People credited with this unit standard are able to: demonstrate and apply knowledge of industrial router technologies; and demonstrate knowledge of the purpose, nature and operation of industrial routers, Dynamic Host Configuration Protocol and Network Address Translation. This standard provides electricity supply industry power technicians with the fundamental knowledge of power protection and control network theory, and hardware. |
| --- | --- |

| Classification | Electricity Supply > Electricity Supply - Power System Maintenance |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Definitions

ACL – access control list.

DHCP – dynamic host configuration protocol.

IP – internet protocol.

ISP – internet service provider.

LAN – local area network.

MAC – media access address.

NAT – network address translation.

VLAN – virtual local area network.

WAN	 – wide area network.

2	It is recommended that Unit 29731 Demonstrate knowledge of protection and control networks is assessed prior to assessment with this standard or equivalent knowledge and skills demonstrated.

Outcomes and performance criteria

Outcome 1

Demonstrate and apply knowledge of industrial router switching technologies.

Performance criteria

1.1	Data types that can be sent and received by an industrial router are described.

1.2	Methods by which the switch can handle frames containing information from the MAC table is explained.

1.3	Principles of borderless switched network design are explained.

Range 	may include – hierarchical, modularity, resiliency and flexibility.

1.4	Configuring of a small industrial LAN using two switches is demonstrated.

Range 	may include – IP address parameters on hosts, verify end to end connectivity.

1.5	Enhanced switching technologies are described.

Range 	may include – VLANs, VLAN trunking Protocol, Rapid Spanning Tree Protocol, Per VLAN Spanning Tree Protocol, 802.1q.

1.6	The process of configuring, verifying and testing port security on a network switch is demonstrated.

1.7	The process of creating, naming and verifying VLAN on industrial switches is demonstrated.

Outcome 2

Demonstrate knowledge of the purpose, nature and operation of industrial routers.

Performance criteria

2.1	The relationship an industrial router can have to local users, industrial networks, multiple LANs and WAN services through ISPs is described.

2.2	The process of configuring two interconnected industrial routers so access is secure and passwords applied is explained.

2.3	Inter-VLAN and static routing is explained.

2.4	Access control using IPv4 and IPv6 is explained and configured on an industrial router.

2.5	Building a network topology to design requirements, configuring device settings, verifying connectivity, configuring IPv6 and default routes to meet traffic requirements is demonstrated.

2.6	The function of components of routing protocols and ACL to support industrial router and network security risk management is explained.

2.7	A named ACL to address a network issue is written, applied and validated.

Outcome 3

Demonstrate knowledge of Dynamic Host Configuration Protocol and Network Address Translation.

Performance criteria

3.1	The steps involved in the DHCP are explained.

3.2	The roles industrial routers may take in the DHCP are explained.

3.3	A network topology is built and configured, a DHCP server and a DHCP relay agent are configured and DHCP services and addresses are verified.

3.4	The function of NAT in a network is explained.

3.5	A network topology is built, configured and verified for both static and dynamic NAT to meet given network requirements.

This unit standard is expiring. Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 20 July 2017 | 31 December 2024 |
| Review | 2 | 2 March 2023 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0120 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.