| Title | Carry out installation, testing, commissioning, and maintenance of solar water heating systems |
| --- | --- |
| Level | 4 | Credits | 4 |

| Purpose | This unit standard is for people who work in the plumbing industry. People credited with this unit standard are able to: – prepare for installation of solar water heating systems; – install, commission, and test solar water heating systems; and – maintain solar water heating systems. |
| --- | --- |

| Classification | Plumbing, Gasfitting and Drainlaying > Plumbing |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	References

Building Act 2004;

Electricity Safety Regulations 2010;

Health Act 1956;

Health and Safety at Work Act 2015;

Plumbers, Gasfitters, and Drainlayers Act 2006;

Plumbers, Gasfitters, and Drainlayers Regulations 2010;

The following standards, which are available at http://www.standards.	govt.nz:

AS/NZS 2712:2007 Solar and heat pump water heaters – Design and construction,

AS/NZS 3500.4:2003 Plumbing and drainage – Part 4 Heated water services,

AS/NZS 5601.1:2010 Gas installations - Part 1: General installations,

NZS 3604:2011 Timber-framed buildings;

The following clauses, and any related compliance documents, which are available at https://www.building.govt.nz/:

New Zealand Building Code Clause E1 Surface Water,

New Zealand Building Code Clause E2 External Moisture,

New Zealand Building Code Clause G10 Piped Services,

New Zealand Building Code Clause G12 Water Supplies;

and all subsequent amendments and replacements.

2	This unit standard requires the application of theory as included in the Plumbers, Gasfitters, and Drainlayers Regulations 2010.

3	Credit for this unit standard does not entitle the candidate to legally perform certain electrical aspects of this work unless registered or supervised by a registered person under the provisions of the Electricity Act 1992.

4	Range

Installation of at least two solar water heating systems covering – direct, indirect, thermosiphon, pump.

5	Definitions

Job requirements – specific requirements of the job at hand not covered by job specifications.

Job specifications – instructions (oral, written, graphic) and may include any of the following: manufacturer instructions; design drawing detail specifications; specifications from a specialist source such as an architect, designer, engineer, or a supervisor; and site or work specific requirements.  Where job specifications are in conflict with applicable legislation, standards, and/or codes, such legislation, standards, and/or codes shall take precedence for the purpose of assessment.

Maintain may refer to all or any of – repair, upgrade, alter, remove.

Other services – any existing installed services.

6	All practical activities are to be carried out in a way that avoids harm to people and damage to property, environment, existing installed services, materials, tools, and equipment.

7	Candidates must hold a current limited certificate or exemption under supervision as issued under the Plumbers, Gasfitters, and Drainlayers Act 2006.

Outcomes and performance criteria

Outcome 1

Prepare for installation of solar water heating systems.

Performance criteria

1.1	Confirm building consent in accordance with job specifications.

1.2	Confirm positioning, pipework layout, and structural and aesthetic requirements in accordance with job specifications and customer requirements.

1.3	Observe safety requirements relating to working at heights and lifting loads in accordance with relevant legislation and codes.

1.4	Prepare materials and equipment in accordance with job specifications and job requirements.

Outcome 2

Install, commission, and test solar water heating systems.

Performance criteria

2.1	Confirm fixing and/or support in accordance with job specifications, and install required brackets and other fixing.

2.2	Install and connect required pipework in accordance with job specifications and with particular attention to weather tightness.

2.3	Identify any wiring requirements that need to be carried out by other trade personnel.

2.4	Commission and test systems as required in accordance with relevant legislation, standards, and codes.

2.5	Inform the customer of operation and maintenance requirements in accordance with job specifications.

Outcome 3

Maintain solar water heating systems.

Performance criteria

3.1	Identify faults in terms of causes and means of rectification.

3.2	Rectify faults in accordance with maintenance requirements, job specifications, and relevant standards and codes.

| Replacement information | This unit standard and unit standard 30610 replaced unit standard 24305. |
| --- | --- |

| Planned review date | 31 December 2022 |
| --- | --- |

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 26 October 2017 | N/A |

| Consent and Moderation Requirements (CMR) reference | 0003 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.

Comments on this unit standard

Please contact The Skills Organisation reviewcomments@skills.org.nz if you wish to suggest changes to the content of this unit standard.