| Title | Install and commission electrically controlled gas appliances and equipment |
| --- | --- |
| Level | 4 | Credits | 10 |

| Purpose | This unit standard is for people who work in the gasfitting industry. People credited with this unit standard are able to: – install electrically controlled gas appliances and equipment; and – commission electrically controlled gas appliances and equipment. |
| --- | --- |

| Classification | Plumbing, Gasfitting and Drainlaying > Gasfitting |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	References

Building Act 2004;

Electricity Act 1992;

Gas Act 1992;

Gas (Safety and Measurement) Regulations 2010;

Health and Safety at Work Act 2015;

Plumbers, Gasfitters, and Drainlayers Act 2006;

Plumbers, Gasfitters, and Drainlayers Regulations 2010;

The following standards, which are available at http://www.standards.govt.nz:

AS/NZS 5601.1:2013Gas installation,

AS/NZS 5601.2:2013 LP Gas installations in caravans and boats for non-propulsive purposes,

NZS 3604:1999 Timber Framed Buildings;

The following clauses, and any related compliance documents, which are available at https://www.building.govt.nz/:

New Zealand Building Code, Clause E2 External moisture,

New Zealand Building Code Clause G11 Gas as an Energy Source;

and all subsequent amendments and replacements.

2	Credit for this unit standard does not entitle the candidate to legally perform certain electrical aspects of this work unless registered or supervised by a registered person under the provisions of the Electricity Act 1992.

3	Range

Two gas cooking appliances which may include but are not limited to – domestic and commercial ovens, ranges, grills, fryers, baking ovens, steam ovens;

two space gas heating appliances;

two central gas heating appliances;

two gas water heating appliances which may include but are not limited to – continuous flow water heaters, storage water heaters, pool heaters, spa pool heaters, indirect heated water heaters, boilers.

4	This unit standard requires the application of theory as included in the Plumbers, Gasfitters, and Drainlayers Regulations 2010.

5	Definitions

Electrically controlled gas appliances – mains power supplied electrically controlled gas appliances generally below 250MJ per hour rated input.

Job specifications – instructions (oral, written, graphic) and may include any of the following: manufacturer instructions; design drawing detail specifications; specifications from a specialist source such as an architect, designer, engineer, or a supervisor; and site or work specific requirements.  Where job specifications are in conflict with applicable legislation, standards, and/or codes, such legislation, standards, and/or codes shall take precedence for the purpose of assessment.

Other services – any existing installed services.

6	Credit for this unit standard does not entitle the candidate to legally perform certain electrical aspects of this work unless registered or supervised by a registered person under the provisions of the Electricity Act 1992.

7	Candidates must hold a current limited certificate or exemption under supervision as issued under the Plumbers, Gasfitters, and Drainlayers Act 2006.

8	All practical activities are to be carried out in a way that avoids harm to people and damage to property, other services, materials, tools, and equipment.

Outcomes and performance criteria

Outcome 1

Install electrically controlled gas appliances and equipment.

Performance criteria

1.1	Select appropriate gas appliances, flues, and ventilation in accordance with job specifications and AS/NZS 5601:2013, Part 1 and Part 2.

1.2	Establish location of gas appliances, flues, and ventilation in accordance with job specifications and AS/NZS 5601:2013. Part 1 and Part 2.

1.3	Install gas appliances, flues, and ventilation in accordance with job specifications.

1.4	As required, install flashing to ensure weather tightness in accordance with Clause E2 of the New Zealand Building Code and any related compliance documents.

1.5	Carry out soundness tests in accordance with AS/NZS 5601:2013, Part 1 and Part 2.

1.6	Purge gas supply system in accordance with AS/NZS 5601:2013, Part 1 and Part 2.

1.7	Connect gas appliances and associated fittings to gas supply connection points in accordance with job specifications.

Outcome 2

Commission electrically controlled gas appliances and equipment.

Performance criteria

2.1	Carry out gas appliance commissioning in accordance with manufacturer instructions.

2.2	Test flues in accordance with AS/NZS 5601:2013, Part 1 and Part 2.

Range	smoke test or draft gauge.

2.3	Determine and calculate ventilation requirements.

2.4	Complete post installation documentation in accordance with job requirements.

Range	may include but is not limited to – gas certificates, guarantees, checklists.

2.5	Instruct the consumer on the proper use of appliance on completion of installation and commissioning.

| Replacement information | This unit standard and unit standard 30707 replaced unit standard 21893. |
| --- | --- |

| Planned review date | 31 December 2022 |
| --- | --- |

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 23 November 2017 | N/A |

| Consent and Moderation Requirements (CMR) reference | 0003 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.

Comments on this unit standard

Please contact The Skills Organisation reviewcomments@skills.org.nz if you wish to suggest changes to the content of this unit standard.