| Title | Demonstrate knowledge of aircraft radio communications and navigation systems |
| --- | --- |
| Level | 4 | Credits | 10 |

| Purpose | People credited with this unit standard are able to: relate the principles of radio frequency communication to their use in aircraft systems; describe the principles and operation of aircraft radio communication systems; describe communications system maintenance procedures; describe the principles and operation of aircraft navigation systems; describe navigation system maintenance procedures; and describe the principles and operation of aircraft passenger address, intercom and entertainment systems. |
| --- | --- |

| Classification | Aeronautical Engineering > Aeronautical Engineering - Core |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	The depth and scope of knowledge required for each performance criterion in this unit standard is that required to carry out system maintenance and component repair or overhaul tasks.

2	The scope of the system that this standard relates to is described in ATA iSpec 2200, and applicable chapters.

Outcomes and performance criteria

Outcome 1

Relate the principles of radio frequency communication to their use in aircraft systems.

Performance criteria

1.1	The use of the radio frequency spectrum is described in terms of its application to aircraft systems.

1.2	Transmission, reception and propagation principles are described in terms of their use in aircraft systems.

Range	amplitude modulation, frequency modulation, single side band.

1.3	The principles of operation of radio components are described in terms of their function in aircraft systems.

Range	transmitters, receivers, transmission lines, transducers, antennas, power supplies.

Outcome 2

Describe the principles and operation of aircraft radio communication systems.

Range	High Frequency (HF), Very High Frequency (VHF).

Performance criteria

2.1	Communication system components are identified in terms of aircraft communication systems.

2.2	The function of each component is described in terms of its operation within an aircraft system.

2.3	The interaction and interface of the communication systems with other aircraft systems is described for normal operating conditions.

Outcome 3

Describe communications system maintenance procedures.

Performance criteria

3.1	Maintenance procedures are described for on-board system maintenance activities.

Range	fault finding, component changes, testing.

3.2	Safety precautions are identified for on-board system maintenance activities.

Range	system isolation, labels, warning signs, system activation procedures.

Outcome 4

Describe the principles and operation of aircraft navigation systems.

Performance criteria

4.1	Navigation systems and equipment are described in terms of their use on aircraft.

Range	VHF Navigation systems, Distance Measuring Equipment, Radio altimeters, Air Traffic Control systems, Automatic Direction Finding, Traffic Advisory and Collision Avoidance Systems, Ground Proximity Warning, Global Positioning systems.

4.2	The function of components is described in terms of their operation within the system.

4.3	The modes of system operation are described for normal operating conditions.

4.4	The principles of system operation are described in terms of aircraft flight navigation requirements.

4.5	The interaction and interface of the navigation systems with other aircraft systems is described for normal operating conditions.

Outcome 5

Describe navigation system maintenance procedures.

Performance criteria

5.1	Procedures to maintain an aircraft system are described for on-board maintenance activities.

Range	fault finding, component changes, testing.

5.2	Safety precautions are identified for on-board system maintenance activities.

Range	system isolation, labels, warning signs, system activation procedures.

Outcome 6

Describe the principles and operation of aircraft passenger address, intercom and entertainment systems.

Performance criteria

6.1	Passenger address, intercom and entertainment system components are identified in terms of aircraft systems.

6.2	The function of each component is described in terms of its operation within an aircraft system.

6.3	The interaction and interface of the passenger address, intercom and entertainment systems with other aircraft systems is described for normal operating conditions.

| Planned review date | 31 December 2027 |
| --- | --- |

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 19 June 1995 | 31 December 2016 |
| Review | 2 | 1 September 1997 | 31 December 2016 |
| Revision | 3 | 8 May 2001 | 31 December 2016 |
| Review | 4 | 19 May 2006 | 31 December 2016 |
| Revision | 5 | 21 September 2007 | 31 December 2016 |
| Review | 6 | 19 September 2013 | 31 December 2021 |
| Review | 7 | 26 March 2020 | N/A |
| Rollover and Revision | 8 | 26 April 2024 | N/A |

| Consent and Moderation Requirements (CMR) reference | 0028 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.

Comments on this unit standard

Please contact Ringa Hora Services Workforce Development Council qualifications@ringahora.nz if you wish to suggest changes to the content of this unit standard.