| Title | Transport aircraft |
| --- | --- |
| Level | 4 | Credits | 4 |

| Purpose | People credited with this unit standard are able to: prepare aircraft for transportation; and transport and reassemble aircraft at destination. |
| --- | --- |

| Classification | Aeronautical Engineering > Aircraft Servicing |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

- All tasks must be carried out in accordance with enterprise procedures.

- Definition

Enterprise procedures – procedures used by the organisation carrying out the work and applicable to the tasks being carried out.  Examples are – standard operating procedures, safety procedures, equipment operating procedures, codes of practice, quality management practices and standards, procedures to comply with legislative and local body requirements.

3	The scope of the system that this standard relates to is described in the applicable chapters of ATA iSpec 2200.

Outcomes and performance criteria

Outcome 1

Prepare aircraft for transportation.

Range		disassembled, inhibited, ground support equipment used, packed, cocooned, palletised, labelled.

Performance criteria

1.1	Items for transport are loaded aboard transportation vehicle.

Range	may include but is not limited to – lifting equipment and vehicle positioning guidance, load distribution, load secured.

1.2	Transportation vehicle is prepared.

Range	may include but is not limited to – dangerous goods procedures followed, driver verified as authorised, attendants and/or escorts arranged.

1.3	Documentation is processed.

Range	documentation may include but is not limited to – packing notes, despatch documentation, waybills;

information required may include but is not limited to – quantities, number of containers.

Outcome 2

Transport and reassemble aircraft at destination.

Performance criteria

2.1	Aircraft and associated components and equipment are transported by road, rail, sea, or air.

Range	may include but is not limited to – route determined, escorts and/or attendants positioned, dangerous goods procedures followed, vehicle speeds controlled, clearances maintained, fire fighting equipment positioned.

2.2	Aircraft is unloaded from transportation vehicle.

2.3	Aircraft is reassembled.

2.4	Documentation is completed.

| Planned review date | 31 December 2024 |
| --- | --- |

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 19 June 1995 | 31 December 2016 |
| Revision | 2 | 7 August 1997 | 31 December 2016 |
| Revision | 3 | 8 May 2001 | 31 December 2016 |
| Review | 4 | 20 June 2006 | 31 December 2016 |
| Review | 5 | 18 June 2014 | 31 December 2021 |
| Review | 6 | 26 March 2020 | N/A |

| Consent and Moderation Requirements (CMR) reference | 0028 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.

Comments on this unit standard

Please contact ServiceIQ qualifications@serviceiq.org.nz if you wish to suggest changes to the content of this unit standard.