| Title | Identify levels of finish, calculate quantities and order stopping and finishing compounds for plaster board |
| --- | --- |
| Level | 3 | Credits | 6 |

| Purpose | People credited with this unit standard are able to identify levels of finish to plaster board walls and ceilings, and calculate quantities of materials required and prepare an order. |
| --- | --- |

| Classification | Construction Trades > Plaster Board |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Definition

Specifications refers to documented instructions (oral, written, graphic) and may include any of the following:  manufacturer’s specifications, recommendations or technical data sheets; material specifications; specifications from a specialist source such as an architect, designer, engineer or a supervisor; site or work specific requirements.

2	Reference material

AS/NZS 2589:2007 Gypsum linings - Application and finishing, available from Standards NZ (http://www.standards.co.nz).

3	Credit for this unit standard can be achieved on site through a registered assessor, or off site with an accredited training provider.

4	Credit for this unit standard indicates compliance with industry practice.  Industry practice refers to the ability to demonstrate knowledge and skills that reflect the productivity, uniformity, finish quality and material economies currently accepted within industry.

Outcomes and performance criteria

Outcome 1

Identify and describe levels of finish to plaster board walls and ceilings.

Performance criteria

1.1	Levels of finish for plasterboard work are described as specified by AS/NZS 2589:2007.

1.2	The description identifies the stopping and finishing compounds required to achieve the specified levels of finish.

Outcome 2

Calculate quantities of materials required and prepare an order.

Performance criteria

2.1	Area to be stopped and finished is identified from working drawings or specifications.

2.2	Quantities of materials are calculated, and an order is prepared to the nearest unit of supply.

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 18 January 1996 | 31 December 2024 |
| Revision | 2 | 5 July 1999 | 31 December 2024 |
| Review | 3 | 29 August 2000 | 31 December 2024 |
| Revision | 4 | 18 May 2005 | 31 December 2024 |
| Review | 5 | 20 April 2006 | 31 December 2024 |
| Review | 6 | 25 January 2008 | 31 December 2024 |
| Review | 7 | 26 May 2022 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0048 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.