| Title | Demonstrate knowledge of, make new and repair existing models for fibrous plaster casting in a factory |
| --- | --- |
| Level | 4 | Credits | 22 |

| Purpose | People credited with this unit standard are able to: describe methods used to make new, and repair existing models for fibrous plaster casting in a factory; make new models and repair existing models for fibrous plaster casting in a factory. |
| --- | --- |

| Classification | Construction Trades > Fibrous Plaster |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Definition

Specifications refers to documented instructions (oral, written, graphic) and may include any of the following: manufacturer’s specifications, recommendations or technical data sheets; material specifications; specifications from a specialist source such as an architect, designer, engineer or a supervisor; site or work specific requirements.

2	All work practices must comply with the following: Health and Safety in Employment Act 1992 and Health and Safety in Employment Regulations 1995; Resource Management Act 1991; Building Act 2004; New Zealand Building Code.

3	Credit for this unit standard indicates compliance with industry practice.  Industry practice refers to the ability to demonstrate knowledge and skills that reflect the productivity, uniformity, finish quality and material economies currently accepted within industry.

Outcomes and performance criteria

Outcome 1

Describe methods used to make new, and repair existing, models for fibrous plaster casting in a factory.

Range	customwood, plaster, clay, plasticine.

Performance criteria

1.1	Methods of making and repairing models are described in accordance with factory requirements and job specifications.

Outcome 2

Make new models for fibrous plaster casting in a factory.

Range	two models of – customwood, plaster, clay, plasticine.

Performance criteria

2.1	Drawings, specifications and details of models are obtained in accordance with factory requirements.

2.2	Working sketches and developments are completed in accordance with drawings, specifications and details.

2.3	Materials to be used for models are identified and an order is prepared in accordance with factory requirements.

2.4	Sample model is produced for approval by client in accordance with working sketches.

2.5	Constructed models conform with approved sample, are checked as fit for purpose for construction of moulds and are confirmed as acceptable to the client.

2.6	All operations are completed, workplace and tools cleaned, and tools stored in accordance with factory requirements.

Outcome 3

Repair existing models for fibrous plaster casting in a factory.

Range	two models.

Performance criteria

3.1	Models are checked to identify those requiring repair.

3.2	Materials required for the repair are identified and an order is placed in accordance with factory requirements.

3.3	Each model is repaired to match original in accordance with factory requirements and is confirmed as acceptable to the client.

3.4	All operations are completed, workplace and tools cleaned, and tools stored in accordance with factory requirements.

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 18 January 1996 | 31 December 2024 |
| Revision | 2 | 5 July 1999 | 31 December 2024 |
| Review | 3 | 29 August 2000 | 31 December 2024 |
| Revision | 4 | 18 May 2005 | 31 December 2024 |
| Review | 5 | 20 April 2006 | 31 December 2024 |
| Review | 6 | 25 January 2008 | 31 December 2024 |
| Review | 7 | 26 May 2022 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0048 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.