| Title | Demonstrate knowledge of hazardous areas and their electrical requirements |
| --- | --- |
| Level | 4 | Credits | 3 |

| Purpose | This unit standard and covers background knowledge relating to hazardous areas, for use in training electrical workers. People credited with this unit standard are able to: – identify hazardous areas; – explain the properties of hazardous materials; – identify and describe sources of ignition; and – demonstrate knowledge of the standards and codes of practice relating to hazardous areas. |
| --- | --- |

| Classification | Electrical Engineering > Core Electrical |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	This unit standard has been developed for learning and assessment off-job.

2	Achievement of this unit standard does not by itself imply competency in performing work in hazardous areas.

3	For competency in hazardous areas work see unit standards 17054 to 17056, 17058, 17059 and 17068 to 17074.

4	References

Electricity Act 1992;

Electricity (Safety) Regulations 2010;

Hazardous Substances and New Organisms Act 1996;

Health and Safety at Work Act 2015, and associated regulations;

AS 1939-1990, Degrees of protection provided by enclosures for electrical equipment (IP Code);

AS/NZS 60079.14:2017, Electrical equipment for explosive atmospheres – Design selection, erection and initial inspection;

AS/NZS 3000:2018, Electrical installations (known as the Australian/New Zealand Wiring Rules) including Amendment 1;

AS/NZS 60079.10.1:2009, Explosive atmospheres – Part 10.1 Classification of areas - Explosive gas atmospheres;

Standards Australia HB 13-2007, Electrical equipment for hazardous areas;

and all subsequent amendments and replacements.

5	The term current regulations and standards is used in this unit standard to refer to the requirements of the above references.

Outcomes and performance criteria

Outcome 1

Identify hazardous areas.

Performance criteria

1.1	The term hazardous area is defined in accordance with current regulations and standards.

1.2	The classification of hazardous areas is described, and examples of each are stated.

Range	zones – 0, or 1, or 2;

divisions – 1 and 2.

1.3	Typical types of hazards that may be present in the hazardous area zones are described.

Range	gas, vapour, liquid, dust, metallic, powder.

1.4	The system of classifying electrical equipment for use in hazardous areas is explained according to current standards.

1.5	Protection methods are described.

Range	flame-proof, increased safety, intrinsically safe, non-sparking.

Outcome 2

Explain the properties of hazardous materials.

Performance criteria

2.1	System of gas grouping is described.

Range	flammable gases, non-flammable gases, reactive gases, toxic gases.

2.2	Properties of flammable gases are described.

Range	upper explosive limit, lower explosive limit, flash point, ignition temperature.

2.3	Hazards of non-flammable and reactive gases are described.

Range	oxidisers, fluorine, chlorine, acetylene, vinyl chloride.

2.4	Properties of dust mixtures are described.

Range	particle size, dust concentration, presence of impurities, oxygen concentration, ignition temperature, minimum energy of ignition.

2.5	Sources of data for hazardous materials are identified.

Range	tables, chemical data sheets, labels, material safety data sheet.

Outcome 3

Identify and describe sources of ignition.

Performance criteria

3.1	Principles of combustion are explained.

Range	fire triangle – oxygen, fuel, ignition; chemical reaction.

3.2	Potential sources of ignition are stated.

Range	flames, welding, sparking, hot surfaces, auto ignition.

3.3	Electrical sources of ignition are stated.

Range	overload, short circuit, static electricity.

Outcome 4

Demonstrate knowledge of the standards and codes of practice relating to hazardous areas.

Performance criteria

4.1	Standards and codes of practice used in New Zealand are identified and described.

Range	New Zealand Electrical Codes of Practice; New Zealand standards; international standards.

4.2	International standards used in New Zealand are stated.

Range	Australian, British, American.

4.3	Requirements of New Zealand standards and codes of practice applicable to hazardous areas are identified and explained.

4.4	Legal responsibilities are identified and explained.

Range	Electrical Codes of Practice, Hazardous Substances and New Organisms Act 1996, Electricity Act 1992, Health and Safety at Work Act 2015, local authority requirements.

4.5	Requirements of AS/NZS 60079.14:2017 for submitting hazardous area drawings for approval are explained.

4.6	Certification abilities of test authorities are described according to current regulations and standards.

4.7	Consequences of non-compliance with prescribed procedures are explained.

Range	Electrical Codes of Practice, Hazardous Substances and New Organisms Act 1996, Electricity Act 1992, Health and Safety at Work Act 2015, local authority requirements.

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 23 April 1996 | 31 December 2013 |
| Review | 2 | 10 February 1999 | 31 December 2013 |
| Review | 3 | 26 May 2005 | 31 December 2027 |
| Rollover and Revision | 4 | 15 March 2012 | 31 December 2027 |
| Revision | 5 | 15 January 2014 | 31 December 2027 |
| Rollover and Revision | 6 | 28 January 2021 | 31 December 2027 |
| Review | 7 | 25 May 2023 | 31 December 2027 |

| Consent and Moderation Requirements (CMR) reference | 0003 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.