| Title | Demonstrate knowledge of, fix and finish fibrous plaster to architectural details on site |
| --- | --- |
| Level | 4 | Credits | 22 |

| Purpose | People credited with this unit standard are able to describe methods used to fix and finish fibrous plaster to architectural details on site; and fix and finish fibrous plaster to architectural details on site. |
| --- | --- |

| Classification | Construction Trades > Fibrous Plaster |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

| Prerequisites | Unit 17584, Demonstrate knowledge of and fix flat fibrous plaster sheets to surfaces on site; and Unit 6133, Demonstrate knowledge of, stop and finish fibrous plaster on site; or demonstrate equivalent knowledge and skills. |
| --- | --- |

Guidance Information

1	Definitions

Access equipment, for the purpose of this unit standard, means equipment used to facilitate access to the work area, and may include ladders, working platforms, scaffolding or mechanical plant.  Approved codes of practice relating to the safe operation of this equipment are available at http://www.osh.govt.nz.

On site refers to a wide range of building and construction environments within which trade skills are applied.

Specifications refers to documented instructions (oral, written, graphic) and may include any of the following:  manufacturer’s specifications, recommendations or technical data sheets; material specifications; specifications from a specialist source such as an architect, designer, engineer or a supervisor; site or work specific requirements.

Work site practice refers to the documented procedures specific to a work site which set out the standard and required practices of that work site.

2	Performance of the elements must meet quality and work requirements of on site environment.  Work requirements are detailed in the current Industry Productivity Guidelines which are available from the Building and Construction Industry Training Organisation, PO Box 2615, Wellington.

3	All work practices must comply with the following: Health and Safety in Employment Act 1992 and Health and Safety in Employment Regulations 1995; Resource Management Act 1991; Building Act 2004; AS/NZS 2589:2007 Gypsum linings – Application and finishing, available from Standards NZ (http://www.standards.co.nz); Approved Code of Practice for the Safe Erection and Use of Scaffolding (Wellington: Occupational Safety and Health Service, Department of Labour, 1995) available at http://www.osh.govt.nz; New Zealand Building Code.

4	Credit for this unit standard indicates compliance with industry practice.  Industry practice refers to the ability to demonstrate knowledge and skills that reflect the productivity, uniformity, finish quality and material economies currently accepted within industry.

Outcomes and performance criteria

Outcome 1

Describe methods used to fix and finish fibrous plaster to architectural details on site.

Performance criteria

1.1	Methods of fixing and finishing are described in accordance with manufacturer’s and job specifications.

Outcome 2

Fix and finish fibrous plaster to architectural details on site.

Range	bulkheads; beam, column and pillar encasements; curved surfaces; openings; skylights; fire surrounds;

four are required.

Performance criteria

2.1	Requirements for the architectural detail are obtained from the working drawings or job specifications.

2.2	Access equipment for wall and ceiling areas is arranged in accordance with the Health and Safety in Employment Regulations.

2.3	Fibrous plaster is fixed and finished to the architectural detail in accordance with working drawings or job specifications and industry practice.

2.4	All operations are completed, workplace and tools cleaned, and tools stored in accordance with work site practice.

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 18 January 1996 | 31 December 2024 |
| Revision | 2 | 5 July 1999 | 31 December 2024 |
| Review | 3 | 29 August 2000 | 31 December 2024 |
| Revision | 4 | 18 May 2005 | 31 December 2024 |
| Review | 5 | 20 April 2006 | 31 December 2024 |
| Review | 6 | 25 January 2008 | 31 December 2024 |
| Review | 7 | 26 May 2022 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0048 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.