| Title | Demonstrate knowledge of, set out and install suspended ceilings on site |
| --- | --- |
| Level | 3 | Credits | 22 |

| Purpose | People credited with this unit standard are able to: describe methods used to install suspended ceilings on site; prepare and set out for installing suspended ceilings on site; and install suspended ceilings on site. |
| --- | --- |

| Classification | Construction Trades > Specialist Interiors |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Definitions

Access equipment, for the purpose of this unit standard, means equipment used to facilitate access to the work area, and may include ladders, working platforms, scaffolding or mechanical plant.  Approved codes of practice relating to the safe operation of this equipment are available at http://www.osh.govt.nz.

On site refers to a wide range of building and construction environments within which trade skills are applied.

Plant is used as in the Health and Safety in Employment Act 1992 to mean: appliances, equipment, fittings, furniture, implements, machines, machinery, tools, vehicles, plus parts, controls, and anything connected to such plant.

Specifications refers to documented instructions (oral, written, graphic) and may include any of the following:  manufacturer’s specifications, recommendations or technical data sheets; material specifications; specifications from a specialist source such as an architect, designer, engineer or a supervisor; site or work specific requirements.

Work site practice refers to the documented procedures specific to a work site, which set out the standard and required practices of that work site.

2	All work practices must comply with the following:

Health and Safety in Employment Act 1992; Health and Safety in Employment Regulations 1995; Resource Management Act 1991; Building Act 2004; AS/NZS 2785:2000 Suspended ceilings – design and installation; AS/NZS 1170.0:2002 Structural design actions – General Principles, available from Standards NZ (http://www.standards.co.nz); Approved Code of Practice for the Safe Erection and Use of Scaffolding (Department of Labour, Wellington, 1995) available at http://www.osh.govt.nz; New Zealand Building Code.

3	Credit for this unit standard indicates compliance with industry practice.  Industry practice refers to the ability to demonstrate knowledge and skills that reflect the productivity, uniformity, finish quality and material economies currently accepted within industry.

4	Performance of the elements must meet quality and work requirements of an on site environment.  Work requirements are detailed in the Industry Productivity Guidelines, which are available from the Building and Construction Industry Training Organisation, PO Box 2615, Wellington.

Outcomes and performance criteria

Outcome 1

Describe methods used to install suspended ceilings on site.

Performance criteria

1.1	Methods of installation are described in accordance with manufacturer’s and job specifications.

Outcome 2

Prepare and set out for installing suspended ceilings on site.

Range	on-site environments include residential, industrial, commercial and multi-storey;

one environment is required.

Performance criteria

2.1	Type of ceiling is identified from working drawings or job specifications.

2.2	Work site measurements are confirmed in accordance with work site practice.

2.3	Heights and grids are set out on site to conform to configuration detailed on working drawings.

2.4	Equipment for handling materials is arranged in accordance with work site practice.

2.5	Materials are accepted and stored on site to ensure specified quality is maintained in accordance with work site practice.

2.6	Access equipment is arranged in accordance with the Health and Safety in Employment Regulations.

2.7	All operations are completed, workplace and tools cleaned, and tools stored in accordance with work site practice.

Outcome 3

Install suspended ceilings on site.

Range	on-site environments include residential, industrial, commercial and multi-storey;

one environment is required.

Performance criteria

3.1	Suspension systems are erected to line and level to conform to working drawings.

3.2	Ceiling lining panels, strips, and sheets are fixed in accordance with job specifications to meet manufacturers’ requirements and industry practice.

3.3	Ceiling lining panels, strips, and sheets are trimmed for edges, projections and recesses as detailed on working drawings.

3.4	Ceiling is checked to ensure it conforms to specification requirements.

3.5	All operations are completed, workplace and tools cleaned, and tools stored in accordance with work site practice.

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 18 January 1996 | 31 December 2024 |
| Revision | 2 | 5 July 1999 | 31 December 2024 |
| Review | 3 | 29 August 2000 | 31 December 2024 |
| Revision | 4 | 18 May 2005 | 31 December 2024 |
| Review | 5 | 19 May 2006 | 31 December 2024 |
| Review | 6 | 20 November 2006 | 31 December 2024 |
| Review | 7 | 26 May 2022 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0048 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.