| Title | Apply avionic repair skills |
| --- | --- |
| Level | 4 | Credits | 18 |

| Purpose | This unit standard is intended for people pursuing unit standards in the avionic repair and avionic maintenance domains. It contains a range of generic repair skills that may be applied to the repair of avionic equipment. People credited with this unit standard are able to: test semiconductor devices; repair avionic printed wiring assemblies; test avionic components; and apply avionic repair procedures. |
| --- | --- |

| Classification | Aeronautical Engineering > Aeronautical Engineering - Core |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

- All tasks must be carried out in accordance with enterprise procedures.

- Definition

Enterprise procedures – procedures used by the organisation carrying out the work and applicable to the tasks being carried out.  Examples are – standard operating procedures, safety procedures, equipment operating procedures, codes of practice, quality management practices and standards, procedures to comply with legislative and local body requirements.

3	Standard industry practices referred to are those in the aviation industry, examples being Great Britain – Civil Aviation Authority, CAP 562: Civil Aircraft Airworthiness Information and Procedures (CAAIP) (London: TSO) and United States – Federal Aviation Administration, Advisory Circular 43.13, Acceptable Methods, Techniques, and Practices – Aircraft Inspection and Repair (US Dept of Transportation).

4	Competencies within this unit standard will be assessed in the work environment or by the use of simulated activities off the job.

Outcomes and performance criteria

Outcome 1

Test semiconductor devices.

Performance criteria

1.1	Semiconductor devices are identified and match circuit specifications.

1.2	Serviceability of semiconductor devices is established in accordance with standard industry practices.

Range	diodes, transistors, using ohmmeter to detect open and short circuits.

1.3	Semiconductor device terminals are identified, and match information contained in circuit specifications.

Outcome 2

Repair avionic printed wiring assemblies.

Performance criteria

2.1	Printed wiring components are removed and installed in accordance with standard industry practices.

2.2	Printed wiring components are soldered in accordance with standard industry practices.

Range	may include but is not limited to – using large iron, soldering station, continuous vacuum extractor, rework and repair station.

2.3	Printed circuit boards are reworked and repaired in accordance with standard industry practices.

Range	may include but is not limited to – single-sided, double-sided, multilayer, flexible.

Outcome 3

Test avionic components.

Performance criteria

3.1	Testing task is determined in accordance with standard industry practices.

Range	avionic equipment identified; test procedures determined.

3.2	Test equipment is selected in terms of the task requirements.

Range	may include but is not limited to – analogue and/or digital multimeter, logic probe, oscilloscope, frequency counter, signal generator, capacitance meter.

3.3	Test equipment is operated in accordance with manufacturer’s instructions.

Range	may include but is not limited to – analogue and/or digital multimeter, logic probe, oscilloscope, frequency counter, signal generator, capacitance meter.

3.4	Avionic components are tested for serviceability in accordance with manufacturer’s specifications.

Outcome 4

Apply avionic repair procedures.

Performance criteria

4.1	Avionic repair procedures are applied in accordance with standard industry practice.

Range	may include but is not limited to – disassembly, inspection, repair, assembly, calibration, test.

| Planned review date | 31 December 2024 |
| --- | --- |

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 21 May 1996 | 31 December 2016 |
| Revision | 2 | 13 August 1997 | 31 December 2016 |
| Revision | 3 | 8 May 2001 | 31 December 2016 |
| Review | 4 | 19 May 2006 | 31 December 2016 |
| Revision | 5 | 21 September 2007 | 31 December 2016 |
| Review | 6 | 19 September 2013 | 31 December 2021 |
| Review | 7 | 26 March 2020 | N/A |

| Consent and Moderation Requirements (CMR) reference | 0028 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.

Comments on this unit standard

Please contact ServiceIQ qualifications@serviceiq.org.nz if you wish to suggest changes to the content of this unit standard.