| Title | Install and replace electricity network pole structures |
| --- | --- |
| Level | 4 | Credits | 10 |

| Purpose | People credited with this unit standard are able to install and replace electricity network pole structures. |
| --- | --- |

| Classification | Electricity Supply > Electricity Supply - Distribution Networks |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Evidence presented for assessment against this unit standard must be consistent with safe working practices and be in accordance with applicable industry and legislative requirements.

2	Legislation, regulations and/or industry standards relevant to this unit standard include but are not limited to the current version of the Health and Safety at Work Act 2015; Electricity Act 1992; Electricity (Safety) Regulations 2010; and any subsequent amendments and replacements; Electricity supply industry codes of practice and documented enterprise procedures, including Safety Manual – Electricity Industry (SM-EI) (2015) Wellington: Electricity Engineers’ Association available from www.eea.co.nz.

3	Definitions

Asset owner refers to a participant who owns or operates assets used for generating or conveying electricity.

Industry requirements include all asset owner requirements; manufacturers’ specifications; and enterprise requirements which cover the documented workplace policies, procedures, specifications, business, and quality management requirements relevant to the workplace in which assessment is carried out.

4	Recommended skills and knowledge:

Unit 10508, Identify electricity systems used in the electricity supply industry;

Unit 10509, Climb and work on electricity network structures; and

Unit 28112, Operate and store machinery, plant, and equipment in an electricity network environment or demonstrate equivalent knowledge and skills.

Outcomes and performance criteria

Outcome 1

Install and replace electricity network pole structures.

Range	evidence for installation of two different pole types and sizes is required.

Performance criteria

  - Pole type and size, structure arrangement and installation method are established.

Range	structure arrangement includes angle, equipment support, intermediate, termination.

1.2	Pole setting arrangements are established.

Range	anchoring, blocking, compaction, depth, guying.

1.3	Underground services are located.

1.4	Hardware is selected to match scope of work and attached to pole.

Range	includes but is not limited to – braces, conductor attachments, insulators, signs;

any two of the following – cross arms, step bolts, cam levers, head spans.

1.5	Pole hole is excavated.

1.6	Pole is erected and set to match design.

1.7	Site is reinstated.

1.8	Completed work is reported concisely in the correct format and filed within the scheduled time-frame.

| Planned review date | 31 December 2024 |
| --- | --- |

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 19 June 1997 | 31 December 2016 |
| Review | 2 | 27 April 2001 | 31 December 2016 |
| Review | 3 | 22 October 2003 | 31 December 2016 |
| Rollover and Revision | 4 | 20 June 2008 | 31 December 2016 |
| Review | 5 | 20 March 2014 | 31 December 2021 |
| Review | 6 | 28 November 2019 | N/A |

| Consent and Moderation Requirements (CMR) reference | 0120 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.

Comments on this unit standard

Please contact Connexis - Infrastructure Industry Training Organisation at qualifications@connexis.org.nz if you wish to suggest changes to the content of this unit standard.