| Title | Joint high voltage paper insulated power cables up to and including 11kV in the electricity supply industry |
| --- | --- |
| Level | 4 | Credits | 6 |

| Purpose | People credited with this unit standard are able to joint high voltage paper insulated power cables up to and including 11kV in the electricity supply industry. |
| --- | --- |

| Classification | Electricity Supply > Electricity Supply - Distribution Networks |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Evidence presented for assessment against this unit standard must be consistent with safe working practices and be in accordance with applicable legislative and industry requirements.

2	Legislation, regulations and/or industry standards relevant to this unit standard include but are not limited to the current version of the Health and Safety at Work Act 2015; Electricity Act 1992; Electricity (Safety) Regulations 2010; and any subsequent amendments and replacements; Electricity supply industry codes of practice and documented enterprise procedures, including Safety Manual – Electricity Industry (SM-EI) (2015) Wellington: Electricity Engineers’ Association available at www.eea.co.nz.

3	Definitions

Asset owner refers to a participant who owns or operates assets used for generating or conveying electricity.

HV is defined as ‘high voltage’ and includes voltages exceeding 1000V AC up to and including 11kV AC.

Industry requirements include all asset owner requirements; manufacturers’ specifications; and enterprise requirements which may include the documented workplace policies, procedures, specifications, business, and quality management requirements relevant to the workplace in which assessment is carried out.

4	It is recommended people achieve Unit 20069, Joint live LV paper insulated power cables in the electricity supply industry; or demonstrate equivalent knowledge and skills, before being assessed against this unit standard.

Outcomes and performance criteria

Outcome 1

Joint high voltage paper insulated power cables up to and including 11kV in the electricity supply industry.

Range	evidence of three joints is required.

Performance criteria

  - Work site is prepared, and a safe working zone is established.

Range	includes – scope of work, cable identification, cable testing.

1.2	Joints are prepared.

Range	cleaning, glanding, stripping.

1.3	Conductors are jointed and re-insulated.

Range	compression, mechanical, sweat, weld.

1.4	Earth continuity, and mechanical and environmental integrity are re-established.

1.5	Cables are tested.

Range	HV pressure testing, insulation, phase testing to manufacturers’ specifications.

1.6	Joint locations are reported.

| Planned review date | 31 December 2025 |
| --- | --- |

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 19 August 1997 | 31 December 2022 |
| Revision | 2 | 16 February 1999 | 31 December 2022 |
| Review | 3 | 27 April 2001 | 31 December 2022 |
| Review | 4 | 22 October 2003 | 31 December 2022 |
| Rollover and Revision | 5 | 25 October 2007 | 31 December 2022 |
| Review | 6 | 27 February 2020 | N/A |

| Consent and Moderation Requirements (CMR) reference | 0120 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.

Comments on this unit standard

Please contact the Connexis – Infrastructure Industry Training Organisation qualifications@connexis.org.nz if you wish to suggest changes to the content of this unit standard.