| Title | Plan the installation of inboard power plants and power trains |
| --- | --- |
| Level | 5 | Credits | 20 |

| Purpose | People credited with this unit standard are able to: specify installation locations and measurements for inboard power plants and power trains, and plan the installation process. |
| --- | --- |

| Classification | Boating Industries > Boatbuilding |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Definitions

Power plant – the engine may be petrol or diesel and it includes subframe, ancillary equipment and systems, water jacketed manifolds, exhaust systems, coolers such as exchangers, intercoolers, oil coolers, gearbox coolers, raw water pumps, charging systems, drives (hydraulic or electric), engine controls and instrumentation, steering system (mechanical, hydraulic, or electronic), and fuel system.

Power train – includes flywheel damper, clutch, gearbox (mechanical and hydraulic reverse production), propeller shaft, and propulsion device (propeller, jet unit, or drive line system).

2	Evidence of installation is either new installation or re-power of an existing installation.

3	Engine bed load support structure can be made of any of the following materials: ferrous metals, non-ferrous metals, timber, composite.

Outcomes and performance criteria

Outcome 1

Specify installation locations and measurements for inboard power plants and power trains.

Performance criteria

1.1	Drawings align with the manufacturers or suppliers requirements and specifications for installation and operation.

1.2	Engine bed load support structure allows for the weight, load, thrust, and torque of the installed power plant including the ancillary systems.

1.3	Installation requirements are coordinated with relevant stakeholders.

Range	examples of stakeholders may include – naval architects or designers, boat builders, clients, client’s representative, engineers.

Outcome 2

Plan the installation process.

Performance criteria

2.1	Plan enables the installation specifications to be achieved.

2.2	Plan includes installation timeline for activities that meets workplace or stakeholder requirements.

Range	activities include – uncoupling, removal, preparation of engine frame, installation, alignment, coupling, testing.

| Planned review date | 31 December 2021 |
| --- | --- |

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 27 August 1997 | 31 December 2018 |
| Revision | 2 | 20 March 2001 | 31 December 2018 |
| Revision | 3 | 16 April 2004 | 31 December 2018 |
| Rollover | 4 | 20 March 2009 | 31 December 2018 |
| Review | 5 | 20 April 2017 | N/A |

| Consent and Moderation Requirements (CMR) reference | 0136 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.

Comments on this unit standard

Please contact the NZ Marine and Composites Industry Training Organisation training@nzmarine.com if you wish to suggest changes to the content of this unit standard.