| Title | Coordinate delivery of and erect precast concrete units on site |
| --- | --- |
| Level | 3 | Credits | 8 |

| Purpose | People credited with this unit standard are able to: conduct pre-erection planning for precast concrete units; coordinate the off-loading of precast concrete units on site; coordinate the stacking of pre-cast concrete units; erect pre-cast concrete units in place on site; and complete work operations on site. |
| --- | --- |

| Classification | Concrete > Concrete Construction |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Definitions

Specifications refers to documented instructions (oral, written, graphic) and may include any of the following: manufacturer’s specifications, recommendations or technical data sheets; material specifications; specifications from a specialist source such as an architect, designer, engineer or a supervisor; site or work specific requirements.

Work site practice refers to the documented procedures specific to a work site which set out the standard and required practices of that work site.

2	Credit for this unit standard indicates compliance with industry practice.  Industry practice refers to the ability to demonstrate knowledge that reflects the productivity, uniformity, finish quality and material economies currently accepted within industry.

3	Assessment against this unit standard must be undertaken on site.  On site refers to a wide range of building and construction environments within which trade skills are required, and includes concrete production and concrete construction sites.

4	Legislation and publications relevant to this unit standard include:

Health and Safety in Employment Act 1992 and Health and Safety in Employment Regulations 1995;

Building Act 2004;

Approved Code of Practice for the safe Handling, Transportation and Erection of Precast Concrete, available from Occupational Safety and Health (http://www.osh.govt.nz/order/catalogue/pdf/concrete-ac.pdf);

NZS 3104:2003 Specification for concrete production and NZS 3109:1997 Concrete construction, available from Standards New Zealand (http://www.standards.co.nz.

Outcomes and performance criteria

Outcome 1

Conduct pre-erection planning for precast concrete units.

Performance criteria

1.1	Planning includes logistics of cranage operations.

Range	rotation of elements, ground conditions, overhead conditions, safety, crane ratings, access requirements.

1.2	The falsework/propping design is interpreted to determine job requirements.

Outcome 2

Coordinate the off-loading of precast concrete units on site.

Performance criteria

2.1	Precast concrete units are verified on delivery as complying with specified requirements.

2.2	Precast concrete units are lifted in accordance with work site practice.

Range	lifting equipment – inserts, bolt holes, lifting clutches, lifting beams, chain angles, hooks, strops, crane, use of dunnage points.

Outcome 3

Coordinate the stacking of precast concrete units.

Performance criteria

3.1	Precast concrete units are stacked in accordance with work site practice, ensuring protection from damage, deterioration and contamination.

Range	factors to consider – accumulation of trapped water, efflorescence, stain or damage by airborne pollutants, rust deposits, chafing and disfiguring, mishandling, dunnage points, access, free movement, use of supports, packaging, temporary protection.

Outcome 4

Erect precast concrete units in place on site.

Performance criteria

4.1	Precast concrete units are lifted in accordance with work site practice.

Range	lifting equipment – inserts, bolt holes, lifting eyes, lifting beams, chain angles, hooks, strops, crane.

4.2	Precast concrete units are placed in position in accordance with specifications and falsework/propping design.

Range	one of – precast beam, precast flooring, precast panel, precast stairs.

4.3	Post erection check is performed to verify erection against specifications, and any required actions are taken in accordance with work site practice.

Range	alignment, location, propping/falsework.

Outcome 5

Complete work operations on site.

Performance criteria

5.1	All operations are safely completed; workplace, tools, plant and equipment are cleaned; and tools, plant and equipment are stored in accordance with work site practice.

5.2	Documentation is completed and processed in accordance with work site practice.

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 21 May 1999 | 31 December 2024 |
| Revision | 2 | 12 February 2003 | 31 December 2024 |
| Review | 3 | 26 July 2004 | 31 December 2024 |
| Review | 4 | 16 April 2010 | 31 December 2024 |
| Review | 5 | 24 November 2022 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0048 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.