| Title | Produce a scale plan of flooring worksite in the flooring industry |
| --- | --- |
| Level | 3 | Credits | 8 |

| Purpose | This unit standard is for people working in the flooring industry. People credited with this unit standard are able to: produce a sketch plan of the floor site; produce a scale plan of the floor site; and complete job records. |
| --- | --- |

| Classification | Construction Trades > Flooring |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Performance of the outcomes of this unit standard must comply with the following legislation and guides: the Building Act 2004; Health and Safety in Employment Act 1992; A Guide to the Health and Safety in Employment Act 1992, 2nd edition (Department of Labour, 2003) available at http://www.osh.dol.govt.nz; and their subsequent amendments.

2	Definition

Workplace procedures are all authorised instructions, processes and work practices carried out in the workshop, factory, shop and worksite.

Outcomes and performance criteria

Outcome 1

Produce a sketch plan of the floor site.

Performance criteria

1.1	Plan includes measurements in accordance with workplace procedures.

Range	may include but is not limited to – running measurements, fixed measurements.

1.2	Plan identifies site characteristics in terms of their significance for the proposed job.

Range	may include but is not limited to – fireplaces, trap doors, fittings, steps, substrate conditions, plumbing fixtures, control joints, penetrations, falls and levels, up-stands, terminations.

Outcome 2

Produce a scale plan of the floor site.

Performance criteria

2.1	Plan produced includes dimensions of site in accordance with workplace procedures.

2.2	Plan produced includes all site characteristics in terms of their location on the site and their dimensions, in accordance with workplace procedures.

2.3	Plan includes client details.

Range	includes but is not limited to – name, address, date, location of work site.

2.4	Plan identifies product location in terms of specified rooms and areas.

Outcome 3

Complete job records.

Performance criteria

3.1	Job sheets are completed in accordance with workplace procedures.

3.2	Records are stored in accordance with workplace procedures.

| Replacement information | This unit standard, unit standard 17010 and unit standard 23273 were replaced by unit standard 32555. |
| --- | --- |

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 29 May 2000 | 31 December 2018 |
| Revision | 2 | 18 February 2004 | 31 December 2018 |
| Review | 3 | 26 March 2007 | 31 December 2018 |
| Review | 4 | 18 February 2011 | 31 December 2024 |
| Review | 5 | 25 November 2021 | 31 December 2024 |
| Rollover | 6 | 30 November 2023 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0175 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.