| Title | Monitor, analyse, and respond to process deviations in an energy and chemical plant |
| --- | --- |
| Level | 5 | Credits | 12 |

| Purpose | People credited with this unit standard are able to: maintain energy and chemical process conditions by monitoring and adjusting equipment and processes, and describe consequences of deviation from stable operating parameters; and describe, respond to, and restore process conditions in an energy and chemical plant. |
| --- | --- |

| Classification | Energy and Chemical Plant > Monitoring of Energy and Chemical Plant |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Legislation and regulations relevant to this unit standard include but are not limited to:

- Health and Safety at Work Act 2015;

- Health and Safety at Work (Hazardous Substances) Regulations 2017 (HSWA);

- Approved Code of Practice for the Design, Safe Operation, Maintenance and Servicing of Boilers, Occupational Health and Safety Service, 2000;

- Resource Management Act 1991;

and any subsequent amendments.

2	Definitions

Distributed control system includes – Supervisory Control and Data Acquisition (SCADA), Man Machine Interfaces (MMI).

Energy and chemical plant may be in – petrochemical, agri-nutrient, power generation, dairy processing, meat processing, and wood fibre manufacturing, or other plants that operate with a combination of high temperatures, pressures, steam and/or chemicals in gas, liquid or solid form.

Organisational requirements – documented policies and procedures.  These may include: equipment manufacturers’ procedures, plant procedures, suppliers’ instructions; site signage; codes of practice; company health and safety plans; on site briefings; and supervisor’s instructions.  This includes all regulatory and legislative obligations that apply to the plant.

Plant – the operational unit, equipment and/or workplace at which the person is working.

- For the purposes of assessment:

- evidence for the practical components of this unit standard must be supplied from the workplace.

- evidence for all outcomes must be presented in accordance with organisational requirements.

- the candidate must control a complex process that uses several systems and plant that has some complex equipment.

Outcomes and performance criteria

Outcome 1

Maintain energy and chemical process conditions by monitoring and adjusting equipment and processes, and describe consequences of deviation from stable operating parameters.

Performance criteria

1.1	Obtain and record process data at scheduled times.

Range	may include – sampling, plant logs, product data, distributed control system.

1.2	Identify, monitor and, where required, adjust operating parameters for each process to ensure plant safety and product specifications are met.

1.3	Describe consequences of deviation from stable operating parameters in terms of effects on product, equipment, and production schedules.

1.4	Identify and analyse trends and adjust equipment and processes where necessary to maintain stable operating parameters.

Outcome 2

Describe, respond to, and restore process conditions in an energy and chemical plant.

Performance criteria

2.1	Describe circumstances in which emergency shutdowns are automatically initiated.

2.2	Describe circumstances in which emergency shutdowns are manually initiated.

2.3	Report situations which cannot be remedied within the operator’s authority to the appropriate personnel for escalation.

2.4	Take corrective actions in the event of a continuing deviation.

2.5	Restore stable process conditions without delay while minimising loss and without compromising safety.

2.6	Identify and diagnose any faults to determine causes.

2.7	Record and communicate problems and corrective actions to appropriate personnel.

| Replacement information | This unit standard replaced unit standard 9593 and unit standard 9594. |
| --- | --- |

| Planned review date | 31 December 2025 |
| --- | --- |

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 24 January 2002 | 31 December 2018 |
| Review | 2 | 20 February 2009 | 31 December 2018 |
| Rollover and Revision | 3 | 20 April 2017 | 31 December 2022 |
| Review | 4 | 27 February 2020 | N/A |

| Consent and Moderation Requirements (CMR) reference | 0079 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.

Comments on this unit standard

Please contact the Primary Industry Training Organisation standards@primaryito.ac.nz if you wish to suggest changes to the content of this unit standard.