| Title | Demonstrate knowledge of electrical test instruments and carry out electrical testing |
| --- | --- |
| Level | 4 | Credits | 4 |

| Purpose | People credited with this unit standard are able to: demonstrate knowledge of electrical test instruments; and carry out electrical testing. |
| --- | --- |

| Classification | Electricity Supply > Electricity Supply - Core Skills |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Evidence presented for assessment against this unit standard must be consistent with safe working practices and be in accordance with applicable legislative and industry requirements.

2	Legislation, regulations and/or industry standards relevant to this unit standard include but are not limited to the current version of the Health and Safety at Work Act 2015; Electricity Act 1992; Electricity (Safety) Regulations 2010; and any subsequent amendments and replacements; Electricity supply industry codes of practice and documented enterprise procedures, including Safety Manual – Electricity Industry (SM-EI) (2015) available from www.eea.co.nz.

3	Definitions

Asset owner refers to a participant who owns or operates assets used for generating or conveying electricity.

Industry requirements include all asset owner requirements; manufacturers’ specifications; and enterprise requirements which cover the documented workplace policies, procedures, specifications, business, and quality management requirements relevant to the workplace in which assessment is carried out.

4	The prove-test-prove method refers to proving the instrument before and after a test to ensure that it works properly and is particularly important when confirming electrical isolation.

Outcomes and performance criteria

Outcome 1

Demonstrate knowledge of electrical test instruments.

Range	may include but is not limited to – voltmeter, ammeter, ohmmeter, multimeter, clip-on ammeter, insulation tester, phase rotation meter, earth resistance tester, high voltage proximity voltage detector, earthing loop impedance tester, ground earth resistance tester. Instruments may be digital or analogue;

evidence of four test instruments is required.

Performance criteria

1.1	The types of test instruments used and their function within the electricity supply industry are described.

1.2	The different electrical categories of test instruments are listed and described.

Range	I, II, III, IV.

1.3	The types of measurements taken by test instruments are physically identified and described.

1.4	Consequences of incorrect use of test instruments are described in terms of polarity reversal.

1.5	Test instruments are set up and their connections to circuit under test are sketched.

Outcome 2

Carry out electrical testing.

Range	tests include – voltage, current, resistance, insulation resistance, earth resistance, loop resistance, rotation, phasing and polarity, instrument category;

evidence of three different types of measurements with different instruments is required.

Performance criteria

2.1	Test instrument is selected to match the type of measurement or indication required and visually inspected for safety.

2.2	Instrument is set for measurement or indication by selection of function and range.

2.3	The ‘prove-test-prove’ method is demonstrated during testing.

2.4	Measurements or indications are taken.

2.5	The results are recorded and analysed for validity.

| Planned review date | 31 December 2024 |
| --- | --- |

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 26 July 2003 | 31 December 2016 |
| Rollover and Revision | 2 | 25 October 2007 | 31 December 2016 |
| Review | 3 | 19 November 2010 | 31 December 2016 |
| Review | 4 | 20 March 2014 | 31 December 2021 |
| Review | 5 | 28 November 2019 | N/A |
| Revision | 6 | 28 January 2021 | N/A |

| Consent and Moderation Requirements (CMR) reference | 0120 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.

Comments on this unit standard

Please contact Connexis - Infrastructure Industry Training Organisation at qualifications@connexis.org.nz if you wish to suggest changes to the content of this unit standard.