| Title | Prepare existing and new surfaces for floor and wall tiling on site |
| --- | --- |
| Level | 4 | Credits | 16 |

| Purpose | People credited with this unit standard are able to: demonstrate knowledge of floor and wall tiling surface preparation, prepare surfaces for tiling on site, and complete work operations. |
| --- | --- |

| Classification | Construction Trades > Floor and Wall Tiling |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Definitions

Specifications refers to documented instructions (oral, written, graphic) and may include any of the following: manufacturer’s specifications, recommendations or technical data sheets; material specifications; specifications from a specialist source such as an architect, designer, engineer or a supervisor; site or work specific requirements.

Work site practice refers to the documented procedures specific to a work site which set out the standard and required practices of that work site.

2	For all on-site unit standards the practical assessment evidence must be provided in the context of commercial business construction operations, in the workplace, under normal workplace conditions.

3	Assessment against this unit standard requires evidence for at least one existing and one new surface.

4	Credit for this unit standard indicates compliance with industry practice.  Industry practice refers to the ability to work unsupervised, demonstrating knowledge and skills that reflect the productivity, uniformity, finish quality and material economies currently accepted within industry.

5	Legislation and publications relevant to this unit standard include:

Health and Safety in Employment Act 1992 and Health and Safety in Employment Regulations 1995;

Building Act 2004;

Resource Management Act 1991;

AS 3958.1:2007, Ceramic tiles - Guide to the installation of ceramic tiles; available from https://www.saiglobal.com/pdftemp/previews/osh/as/as3000/3900/3958.1-2007.pdf.

Outcomes and performance criteria

Outcome 1

Demonstrate knowledge of floor and wall tiling surface preparation.

Performance criteria

  - Procedures for surface preparation for tiling are explained in terms of industry practice.

Range	surface material, surface finish, environment, location, any required curing.

1.2	Procedures for the disposal of waste materials from tiling surface preparation are explained in terms of industry practice.

Outcome 2

Prepare surfaces for tiling on site.

Range	concrete, fibre cement, plaster board, timber flooring;

three of – tile, acoustic membrane, butyl rubber, rendered surface, cork tile, metal, glass, painted surface, plastic.

Performance criteria

  - Surfaces for preparation are identified and checked for compliance with specifications.

Range	surface material, surface finish, environment, location.

  - Actions taken in the event that surfaces are not compliant with specifications are in accordance with work site practice.

2.3	Any work of other trades is identified and protected against damage from tiling operations.

2.4	Method used for preparing surfaces meets the requirements for surface condition, location, and tile type.

2.5	Surface is prepared to a finish suitable for application of tiles in accordance with specifications.

2.6	Site is protected against run-off in accordance with legislation, and surfaces are cleaned in accordance with job and site requirements.

Outcome 3

Complete work operations.

Performance criteria

3.1	All operations are safely completed; workplace, tools, plant and equipment are cleaned; and tools, plant and equipment are stored in accordance with work site practice.

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 16 December 2005 | 31 December 2024 |
| Review | 2 | 18 February 2011 | 31 December 2024 |
| Review | 3 | 30 June 2022 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0048 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.