| Title | Set out floor and wall tiles on site |
| --- | --- |
| Level | 4 | Credits | 16 |

| Purpose | People credited with this unit standard are able to: set up the work area for floor and wall tile set-out, set out tiles on site, and complete work operations. |
| --- | --- |

| Classification | Construction Trades > Floor and Wall Tiling |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Definitions

Pattern work refers to a repetitive design created using tiles, and can include arches and circular work.

Specifications refers to documented instructions (oral, written, graphic) and may include any of the following: manufacturer’s specifications, recommendations or technical data sheets; material specifications; specifications from a specialist source such as an architect, designer, engineer or a supervisor; site or work specific requirements.

Work site practice refers to the documented procedures specific to a work site which set out the standard and required practices of that work site.

2	Credit for this unit standard indicates compliance with industry practice.  Industry practice refers to the ability to work unsupervised, demonstrating knowledge and skills that reflect the productivity, uniformity, finish quality and material economies currently accepted within industry.

3	Legislation and publications relevant to this unit standard include:

Health and Safety in Employment Act 1992 and Health and Safety in Employment Regulations 1995;

Building Act 2004;

Resource Management Act 1991;

AS 3958.1:2007, Ceramic tiles - Guide to the installation of ceramic tiles; available from https://www.saiglobal.com/pdftemp/previews/osh/as/as3000/3900/3958.1-2007.pdf.

Outcomes and performance criteria

Outcome 1

Set up the work area for floor and wall tile set-out.

Performance criteria

1.1	Area to be tiled is confirmed as being in accordance with the plans and specifications.

1.2	Surface to be tiled is checked for compliance with specifications.

1.3	Actions taken in the event that surfaces are not compliant with specifications are in accordance with work site practice.

1.4	Plant and materials are located to minimise the impact of factors that may hinder work flow.

Range	accessibility, services, hazard control, protection against weather.

1.5	Any work of other trades is protected prior to commencement of work.

1.6	Any required access equipment is erected to comply with the Health and Safety in Employment Act.

Outcome 2

Set out tiles on site.

Performance criteria

2.1	Checks are performed to verify that tiles conform to job specifications for type, size, calibration, colour, batch and suitability for purpose.

2.2	Tiles are set out to meet the requirements of the job specifications.

Range	laying surface, nominated tiling pattern, structure movement, logical tile set-out;

allowance for stress points and control joints.

Outcome 3

Complete work operations.

Performance criteria

3.1	All operations are safely completed; workplace, tools, plant and equipment are cleaned; and tools, plant and equipment are stored in accordance with work site practice.

| Replacement information | This unit standard replaced unit standard 6113. |
| --- | --- |

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 16 December 2005 | 31 December 2024 |
| Review | 2 | 18 February 2011 | 31 December 2024 |
| Review | 3 | 30 June 2022 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0048 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.