| Title | Describe and apply a proprietary levelling base plaster to a solid substrate on site |
| --- | --- |
| Level | 4 | Credits | 20 |

| Purpose | People credited with this unit standard are able to: demonstrate knowledge of proprietary levelling base plaster systems; interpret plans for solid areas to be levelled and check surface conditions on site; prepare the surface of areas to be levelled on site; mask the adjoining areas to solid substrate on site; mix and condition levelling base coat plaster on site; and apply levelling base coat plaster to a solid substrate on site. |
| --- | --- |

| Classification | Construction Trades > Proprietary Plaster Cladding Systems |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Definitions

On site refers to a wide range of building and construction environments within which the Proprietary Plaster Cladding Systems trade skills are applied.

Specifications refers to documented instructions (oral, written, graphic) and may include any of the following:  manufacturer’s specifications, recommendations or technical data sheets; material specifications; specifications from a specialist source such as an architect, designer, engineer or a supervisor; site or work specific requirements.

Work site practice refers to the documented procedures specific to a work site, which set out the standard and required practices of that work site.

2	Legislation, regulations, codes and standards relevant to this unit standard include:

Health and Safety in Employment Act 1992;

Health and Safety in Employment Regulations 1995;

Resource Management Act 1991;

Hazardous Substances and New Organisms Act 1996; Building Act 2004;

New Zealand Standards, NZS 4218:2004 Energy efficiency – Small building envelope and NZS 3604:1999 Timber Framed Buildings, available from Standards NZ (http://www.standards.co.nz);

New Zealand Building Code;

Territorial Authorities’ building regulations.

3	Credit for this unit standard indicates compliance with industry practice.  Industry practice refers to the ability to demonstrate knowledge and skills that reflect the productivity, uniformity, finish quality and material economies currently accepted within industry.

Outcomes and performance criteria

Outcome 1

Demonstrate knowledge of proprietary levelling base plaster systems.

Performance criteria

1.1	The purpose of proprietary levelling base plaster systems is described.

1.2	Components of proprietary levelling base plaster systems are identified and described.

Outcome 2

Interpret plans for solid areas to be levelled and check surface conditions on site.

Performance criteria

2.1	Areas to be levelled are identified from the plan and described according to job specifications.

Range	two of – concrete block, concrete surfaces, brick work.

2.2	The required surface conditions of areas to be levelled are identified, described and checked according to job specifications.

Range	dryness, flatness, cleanliness.

2.3	The ancillaries and coincidentals to the substrate are identified and described according to job specifications.

Range	three of – penetrations, joinery, control joints, transitions, flashings.

Outcome 3

Prepare the surface of areas to be levelled on site.

Performance criteria

3.1	Procedures used to clean the surface are identified and meet job requirements.

Range	three of – washing, sandblasting, water blasting, acid etching, chemical cleaning.

3.2	Procedures used to prepare the surface for a thin coat application are identified and applied to meet job requirements.

Range	two of – fairing, blocking, key coating, scratchcoating.

Outcome 4

Mask the adjoining areas to solid substrate on site.

Performance criteria

4.1	Masking products are identified and their application and purpose are described in terms of meeting job requirements.

Range	PVC tape, paper tape, cloth tape, masking paper, plastic sheet, tape primer.

4.2	Types of masking equipment are identified and their use and purpose are described in terms of meeting job requirements.

Range	masking machines, tape dispensers.

4.3	Adjoining surfaces are masked and other trades’ work is protected, in accordance with manufacturer’s specifications and job requirements.

Outcome 5

Mix and condition levelling base coat plaster on site.

Performance criteria

5.1	The measuring and mixing of selected proprietary levelling base coat plasters is described and completed in accordance with manufacturer’s specifications and job requirements.

Range	weights, volumes, coverage quantity, drill mixers, water content, proprietary additives, personal protection.

5.2	The storage and care of mixed levelling base coat plaster is described and is consistent with work site practice and manufacturer’s specifications.

Range	pot life, retempering, temperature.

Outcome 6

Apply levelling base coat plaster to a solid substrate on site.

Performance criteria

6.1	Levelling base coat plaster is applied to the prepared solid surface in accordance with manufacturer’s and job specifications, and using the required application tools.

Range	two of – hawke, trowel, hopper gun, broadknife.

6.2	Curing requirements for levelling base coat plaster are determined in accordance with the material used, time of application, manufacturer’s specifications and working conditions.

Range	three of – shade, moist cure, weather protection, overcoat times, temperature.

| Replacement information | This unit standard replaced unit standard 17510. |
| --- | --- |

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 24 January 2006 | 31 December 2024 |
| Review | 2 | 26 January 2007 | 31 December 2024 |
| Review | 3 | 30 June 2022 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0048 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.