| Title | Demonstrate knowledge of on site framing and substrate for Proprietary Plaster Cladding Systems |
| --- | --- |
| Level | 3 | Credits | 10 |

| Purpose | People credited with this unit standard are able to demonstrate knowledge of on site framing requirements for Proprietary Plaster Cladding Systems; and on site requirements for fibre cement and EIFS substrate. |
| --- | --- |

| Classification | Construction Trades > Proprietary Plaster Cladding Systems |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Definitions

EIFS means Exterior Insulation and Finishing System.

Specifications refers to documented instructions (oral, written, graphic) and may include any of the following:  manufacturer’s specifications, recommendations or technical data sheets; material specifications; specifications from a specialist source such as an architect, designer, engineer or a supervisor; site or work specific requirements.

Substrate refers to the surface or medium that serves as a base upon which the Proprietary Plaster Cladding System coating is applied.

2	Legislation, regulations, codes and standards relevant to this unit standard include:

Health and Safety in Employment Act 1992;

Health and Safety in Employment Regulations 1995;

Resource Management Act 1991;

Hazardous Substances and New Organisms Act 1996; Building Act 2004;

New Zealand Standards, NZS 4218:2004 Energy efficiency – Small building envelope and NZS 3604:1999 Timber Framed Buildings, available from Standards NZ (http://www.standards.co.nz);

New Zealand Building Code;

Territorial Authorities’ building regulations.

Outcomes and performance criteria

Outcome 1

Demonstrate knowledge of on site framing requirements for Proprietary Plaster Cladding Systems.

Range	EIFS system, fibre cement sheet system.

Performance criteria

1.1	Framing requirements for claddings are identified and described in accordance with job plans, specifications, and manufacturer’s technical data sheets.

Range	straightness, cavity structure, bargeboard clearance, ground clearance, flashing requirements, stud spacing, nog spacing, foundation alignment, edge fixing, internal corner fixing, moisture content, wind load requirements.

Outcome 2

Demonstrate knowledge of on site requirements for fibre cement substrate.

Performance criteria

2.1	The ancillaries and accessories for fibre cement substrate are identified, and described in accordance with the job specifications and manufacturer’s technical data sheets.

Range	all flashings, control joints, PVC beads, reinforcement beads, fastenings.

2.2	The fixing procedures for fibre cement substrate and ancillaries are described in accordance with job specifications and manufacturers’ recommendations.

Outcome 3

Demonstrate knowledge of on site requirements for EIFS substrate.

Performance criteria

3.1	The ancillaries and accessories to the specified EIFS cladding substrate are identified and described in accordance with the job specifications and the EIFS manufacturer’s technical data sheets.

Range	all flashings, control joints, PVC beads, reinforcement beads, fastenings.

3.2	The fixing procedures for EIFS substrate and ancillaries are described in accordance with job specifications and manufacturers’ recommendations.

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 24 January 2006 | 31 December 2024 |
| Review | 2 | 26 January 2007 | 31 December 2024 |
| Review | 3 | 30 June 2022 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0048 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.