| Title | Complete a scaffolding inspection compliance report |
| --- | --- |
| Level | 3 | Credits | 4 |

| Purpose | People credited with this unit standard are able to: – complete an inspection compliance report for tube and coupler scaffolding; and – complete an inspection compliance report for proprietary scaffolding. |
| --- | --- |

| Classification | Lifting Equipment > Elementary Scaffolding |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	This unit standard has been developed for learning and assessment on-job or off-job in a simulated environment.  Where supervision is required by law, the supervisor must hold the appropriate Certificate of Competence for the scaffolding work undertaken.

2	This unit standard is intended for use with standing and hanging scaffolding built with tube and coupler, or proprietary systems.  It specifically excludes suspended scaffolding.

3	All tasks are to be carried out in accordance with:

a	quality management systems;

b	designer requirements and manufacturer operating instructions; and legislation, regulations, bylaws, Health and Safety at Work Act 2015, and Health and Safety in Employment Regulations 1995;

c	the most up to date version of the Good Practice Guidelines - Scaffolding in New Zealand (GPG), 2016 available from https://www.worksafe.govt.nz/topic-and-industry/working-at-height/scaffolding-in-new-zealand/;

and all subsequent amendments and replacements.

4	Definition

Scaffolding is as described in the GPG and in the Health and Safety in Employment Regulations 1995.

5	Training and assessment

This unit standard must be assessed against the inspection reports for scaffolds contained in Appendix F of the GPG.  To achieve competency in this unit standard, inspection reports must be completed for both tube and coupler, and proprietary scaffolding.  The focus for competency is the completion of the inspection compliance report itself.  This may be conducted on any appropriate scaffolding, which need not have been erected by the candidate.

Outcomes and performance criteria

Outcome 1

Complete an inspection compliance report for tube and coupler scaffolding.

Performance criteria

1.1	Inspect a tube and coupler scaffolding for compliance with the inspection report.

1.2	Complete an inspection report for a tube and coupler scaffolding.

1.3	Identify, record, and recommend remedial action to any non-compliant aspects.

Outcome 2

Complete an inspection compliance report for proprietary scaffolding.

Performance criteria

2.1	Inspect a proprietary scaffolding for compliance with the inspection report.

2.2	Complete an inspection report for a proprietary scaffolding.

2.3	Identify, record, and recommend remedial action to any non-compliant aspects.

| Replacement information | This unit standard, unit standard 20855 and unit standard 20856 replaced unit standard 4200 and unit standard 4202. |
| --- | --- |

| Planned review date | 31 December 2026 |
| --- | --- |

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 25 July 2007 | 31 December 2016 |
| Review | 2 | 16 July 2015 | 31 December 2019 |
| Rollover and Revision | 3 | 23 November 2017 | 31 December 2025 |
| Review | 4 | 24 February 2022 | N/A |
| Revision | 5 | 24 August 2023 | N/A |

| Consent and Moderation Requirements (CMR) reference | 0003 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.

Comments on this unit standard

Please contact Waihanga Ara Rau Construction and Infrastructure Workforce Development Council qualifications@waihangaararau.nz if you wish to suggest changes to the content of this unit standard.