| Title | Check, test, and inspect special hazards fire detection and alarm systems |
| --- | --- |
| Level | 4 | Credits | 20 |

| Purpose | This unit standard is for the training of fire alarm technicians and covers monthly checking and testing and annual checking, testing, and inspection (surveys) of special hazards fire detection and alarm systems in accordance with standard NZS 4512:2010 and standards relevant to special hazards systems fire detection and alarm systems. People credited with this unit standard are able to prepare for and conduct checks, tests, and inspections of special hazards fire detection and alarm systems. |
| --- | --- |

| Classification | Mechanical Engineering > Fire Detection and Alarm Systems |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Explanatory notes

1	References

Ministry of Business, Innovation and Employment (MBIE) Acceptable Solutions (AS) and Verification Methods (VM).  Available at http://www.dbh.govt.nz/AS/VM-documents

NZS 4512:2010, Fire Detection and Alarm Systems in Buildings.

2	Definitions

Annual checks, tests, and inspections are also referred to as annual surveys.

Enterprise procedures refer to the documented procedures used by the organisation carrying out the work and applicable to the tasks being carried out.  They may include but are not limited to – standard operating procedures, site safety procedures, equipment operating procedures, codes of practice, quality assurance procedures, housekeeping standards, charging of time and materials, management of drawings and documentation, procedures to comply with legislative and local body requirements.

Fire detection and alarm system refers to an installation of apparatus, which performs specified fire related functions in response to the operation of a detector, manual call point, or other input.  It includes manual call points, detectors, control and indication equipment, alerting devices, interconnections, fittings, labels, energy sources, and remote signalling devices and may include emergency warning and intercommunication systems (EWIS) where applicable.

Inspection refers to an organised examination of characteristics of fire protection systems against established standards.

Special hazards fire detection and alarm system refers to fire detection and alarm systems which apply electrical actuation to operate mechanical extinguishing systems.  It includes water based, chemical, and clean agent gas flood installations.

Standards refer to NZS 4512:2010, and to standards relevant to the special hazards systems.

Systems documentation refers to the documentation required to be maintained by NZS 4512:2010 and other relevant standards, including log book, test reports, equipment details and drawings, specifications, contract agreement, software configurations and versions, additions and alterations, contract agreement, fire reports, building consents standards, codes of practice, installation instructions, test and commissioning procedures, test and maintenance records.

Tests refer to the carrying out of operations, measurements, or functions to confirm correct function or performance of components and systems in accordance with the standards.

3	Range

a	All activities must comply with relevant legislative and/or regulatory requirements and recognised codes of practice.

b	All activities must demonstrate safe working practices.

c	All activities must be completed and reported within agreed timeframes.

4	Assessment

For assessment purposes, competence must be demonstrated on at least one each of a weekly, quarterly, six-monthly and annual check, test, and inspection.

Outcomes and evidence requirements

Outcome 1

Prepare for checks, tests, and inspections.

Evidence requirements

1.1	Site access and timing of the inspections are agreed with site managers or customers in accordance with enterprise procedures.

1.2	Site occupational safety and health implications for self and others are identified and control measures put in place.

1.3	Details of systems and scope of testing are identified from company records and systems documentation, and any special precautions that are relevant to the installations are identified and recorded in accordance with enterprise procedures.

Outcome 2

Conduct checks, tests, and inspections of special hazards fire detection and alarm systems.

Evidence requirements

2.1	Checks, tests, and inspections are conducted in accordance with systems documentation and enterprise procedures.

2.2	Reports are prepared, entered in the system log, and copies sent to the customer in accordance with systems documentation and enterprise procedures.

2.3	Malfunctions or defects are reported and arrangements made for their rectification in accordance with systems documentation and enterprise procedures.

2.4	Systems are restored to operational status in accordance with systems documentation.

2.5	Site personnel are advised of system status and test completion.

| Replacement information | This unit standard replaced unit standard 9395. |
| --- | --- |

| Planned review date | 31 December 2020 |
| --- | --- |

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 27 October 2006 | 31 December 2017 |
| Review | 2 | 15 October 2015 | N/A |

| Consent and Moderation Requirements (CMR) reference | 0013 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.

Please note

Providers must be granted consent to assess against standards (accredited) by NZQA, before they can report credits from assessment against unit standards or deliver courses of study leading to that assessment.

Industry Training Organisations must be granted consent to assess against standards by NZQA before they can register credits from assessment against unit standards.

Providers and Industry Training Organisations, which have been granted consent and which are assessing against unit standards must engage with the moderation system that applies to those standards.

Requirements for consent to assess and an outline of the moderation system that applies to this standard are outlined in the Consent and Moderation Requirements (CMRs).  The CMR also includes useful information about special requirements for organisations wishing to develop education and training programmes, such as minimum qualifications for tutors and assessors, and special resource requirements.

Comments on this unit standard

Please contact Competenz at qualifications@competenz.org.nz if you wish to suggest changes to the content of this unit standard.