| Title | Repair a damaged motor vehicle panel using glass reinforced plastic (GRP) |
| --- | --- |
| Level | 4 | Credits | 2 |

| Purpose | People credited with this unit standard are able to repair a damaged motor vehicle panel using GRP. |
| --- | --- |

| Classification | Motor Industry > Vehicle Bodywork |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Legislation and references

Performance of the outcomes of this unit standard must comply with the following:

Health and Safety at Work Act 2015.

2	Any new, amended or replacement Acts, regulations, standards, codes of practice, guidelines, or authority requirements or conditions affecting this unit standard will take precedence for assessment purposes, pending review of this unit standard.

3	Definitions

Company requirements refer to instructions to staff on policy and procedures that are available in the workplace.  These requirements may include – company policies and procedures, work instructions, product quality specifications and legislative requirements.

Service information may include – technical information for a vehicle, machine, or product detailing operation; installation and servicing procedures; manufacturer instructions; technical terms and descriptions; and detailed illustrations.

4	Assessment

Evidence presented for assessment against this unit standard must be consistent with safe working practices and be in accordance with applicable manufacturers specifications, service information, company requirements and legislative requirements.

5	For this unit standard, it is essential that the practical assessment evidence is obtained in the workplace under normal workplace conditions.

6	Recommended skills and knowledge

It is recommended that people first hold credit for Unit 23986, Demonstrate knowledge of glass reinforced plastic (GRP) and working with GRP repair kits for motor vehicles, or equivalent knowledge and skills.

Outcomes and performance criteria

Outcome 1

Repair a damaged motor vehicle panel using GRP.

Performance criteria

1.1	Panel surface is prepared for repairs.

Range	may include – pre-cleaning, gaining adhesion, no loose or ragged edges, clamping.

1.2	Resin and catalyst are mixed, and the fibreglass is applied.

Range	temperature, humidity.

1.3	Filler is applied and sanded down to a smooth level surface that blends in with the undamaged areas.

1.4	The repair is checked to ensure there are no deep sanding scratches or irregularities that will impair painting.

| Replacement information | This unit standard and unit standard 23986 replaced unit standard 5764. |
| --- | --- |

| Planned review date | 31 December 2027 |
| --- | --- |

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 26 November 2007 | 31 December 2019 |
| Review | 2 | 16 February 2017 | 31 December 2023 |
| Review | 3 | 10 December 2020 | 31 December 2027 |
| Review | 4 | 25 May 2023 | N/A |

| Consent and Moderation Requirements (CMR) reference | 0014 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.

Comments on this unit standard

Please contact Hanga-Aro-Rau Manufacturing, Engineering and Logistics Workforce Development Council qualifications@hangaarorau.nz if you wish to suggest changes to the content of this unit standard.