| Title | Demonstrate knowledge of two storey veneer construction |
| --- | --- |
| Level | 3 | Credits | 8 |

| Purpose | People credited with this unit standard are able to demonstrate knowledge of: lintels; shelf-angles; slip joints; and a two storey veneer construction system. |
| --- | --- |

| Classification | Masonry > Brick and Block Laying |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Definitions

Specifications refer to any, or all of the following:

manufacturer’s specifications and/or recommendations;

site and/or workplace specific requirements.

Industry practice refers to the expected standard required at the location in which credit for this standard is sought; such standards may be set down in: industry codes of practice, enterprise procedures, which refer to documented procedures specific to the enterprise which set out the standard business practice, and activities of that enterprise.

2	New Zealand Standards relevant to this unit standard include the following:

NZS 4210:2001, Masonry Construction: Materials and Workmanship;

NZS 3604:1999, Timber Framed Buildings.

Outcomes and performance criteria

Outcome 1

Demonstrate knowledge of lintels for two storey veneer construction.

Performance criteria

1.1	Sizes and bearing requirements for lintels are identified in accordance with the job specifications and NZS 4210 requirements.

1.2	The process for setting up lintels is described in accordance with the job specifications and industry practice.

1.3	The process for propping lintels is described in accordance with the job specifications and industry practice.

1.4	The process for flashing lintels is described in accordance with the job specifications and industry practice.

Outcome 2

Demonstrate knowledge of shelf-angles for two storey veneer construction.

Performance criteria

2.1	Sizes for shelf-angles are identified in accordance with the job specifications and NZS 4210 requirements.

2.2	The process for fixing shelf-angles to a frame is described in accordance with the job specifications and industry practice.

2.3	The process for flashing shelf-angles is described in accordance with the job specifications and industry practice.

Outcome 3

Demonstrate knowledge of slip joints for two storey veneer construction.

Performance criteria

3.1	Slip joint material requirements are identified in accordance with the job specifications and the NZS 4210 requirements.

3.2	The process for placing slip joints is described in accordance with the job specifications and industry practice.

3.3	The process for fixing ties is described in accordance with the job specifications and industry practice.

Outcome 4

Demonstrate knowledge of a two storey veneer construction system.

Performance criteria

4.1	The process for setting out a two storey veneer system is described in terms of the steps required.

4.2	Construction requirements for setting out a two storey veneer system are identified and described in accordance with the job specifications and industry practice.

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 14 December 2007 | 31 December 2011 |
| Revision | 2 | 21 July 2011 | 31 December 2024 |
| Review | 3 | 30 June 2022 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0048 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.