| Title | Describe domestic wastewater treatment processes |
| --- | --- |
| Level | 4 | Credits | 8 |

| Purpose | People credited with this unit standard are able to describe domestic wastewater treatment processes. |
| --- | --- |

| Classification | Water Industry > Wastewater Treatment |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

- Evidence presented for assessment against this unit standard must be consistent with safe working practices and be in accordance with applicable legislative and industry requirements.

2	Legislation, regulations and industry standards relevant to this unit standard include but are not limited to the:

- Resource Management Act 1991;

- Building Act 2004 and relevant Building Codes;

- Health Act 1956;

- Historic Places Act 1993, and subsequent amendments;

- regional and district plans;

- regulatory authority requirements;

- AS/NZS 1547:2012 On-site domestic wastewater management;

- AS/NZS 1546.1:2008 On-site domestic wastewater treatment units – Septic tanks;

- AS/NZS 1546.2:2008 On-site domestic wastewater treatment units – Waterless composting toilets;

- AS/NZS 1546.3:2008 On-site domestic wastewater treatment units – Aerated wastewater treatment systems; available at http://www.standards.co.nz.

3	Definition

Industry requirements include manufacturers’ specifications; and enterprise requirements which cover the documented workplace policies, procedures, specifications, business, and quality management requirements relevant to the workplace in which assessment is carried out.

4	It is recommended that the assessor uses design guidelines issued by the regional or local authorities in the candidate’s locality.

5	Credit for this unit standard does not qualify the candidate to work in a drainlaying situation that comes under the drainlayer’s licence requirements issued under the Plumbers, Gasfitters, and Drainlayers Act 2006 and any subsequent amendments.

Outcomes and performance criteria

Outcome 1

Describe domestic wastewater treatment processes.

Performance criteria

  - Primary treatment processes are described in terms of the operation of septic tanks and grease traps from inflow of raw wastewater to the discharge of treated wastewater.

Range	includes but is not limited to – types, features and operation of tanks and traps, factors affecting performance, risks and associated mitigation, installation.

  - Secondary treatment processes are described.

Range	includes but is not limited to – design, methods, operation and maintenance, factors affecting performance, risks and associated mitigation, suitability for situations, installation;

evidence of three processes is required.

  - Disinfection treatment processes are described.

Range	includes but is not limited to – methods, components, operation and maintenance, factors affecting performance, risks and associated mitigation;

evidence of three processes is required.

  - Nutrient reduction treatment processes are described.

Range	includes but is not limited to – methods, components, operation and maintenance, factors affecting performance, risks and associated mitigation;

evidence of processes to reduce nitrogen and phosphorus is required.

  - Alternative treatment systems are described.

Range	includes but is not limited to – methods, benefits, design, operation and maintenance, conditions required for effective operation, factors affecting performance, risks and associated mitigation;

evidence of three types of alternative treatment systems is required.

1.6	Soil treatment processes are described in terms of interactions between soil, plants and wastewater.

| Planned review date | 31 December 2025 |
| --- | --- |

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 17 October 2008 | 31 December 2018 |
| Rollover and Revision | 2 | 16 March 2017 | 31 December 2022 |
| Review | 3 | 23 July 2020 | N/A |

| Consent and Moderation Requirements (CMR) reference | 0101 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.

Comments on this unit standard

Please contact Connexis - Infrastructure Industry Training Organisation qualifications@connexis.org.nz if you wish to suggest changes to the content of this unit standard.