| Title | Demonstrate knowledge of and design documentation for the commissioning of significant electrical installations |
| --- | --- |
| Level | 5 | Credits | 5 |

| Purpose | This unit standard and is intended for use in the training and assessment of electricians beyond trade level who have responsibility for the management of significant industrial, commercial, residential, or domestic commissioning projects, including bringing assets which often represent substantial investment by their client or employer into service. It is designed to ensure that such people have sufficient knowledge of commissioning and handover to safely and competently perform these functions. People credited with this unit standard are able to: – demonstrate knowledge of standard commissioning procedures and documentation used to manage significant electrical installations – design and develop a documentation pack for commissioning and handover of a significant electrical installation. |
| --- | --- |

| Classification | Electrical Engineering > Electrical Installation and Maintenance |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Recommended skills and knowledge:

It is expected that candidates for assessment against this unit standard will already:

–	have achieved an electrical qualification such as the National Certificate in Electrical Engineering (Electrician for Registration) (Level 4) [Ref: 1195], or demonstrate equivalent or higher skills and knowledge

–	have learnt project management principles and techniques

–	be familiar with the requirements of the Health and Safety at Work Act 2015.

2	This unit standard has been developed for learning and assessment off-job.

3	References

AS/NZS 3000 (version as cited in the Electricity (Safety) Regulations), Electrical installations (known as the Australian/New Zealand Wiring Rules), including Amendment 1

Electricity Act 1992

Electricity (Safety) Regulations 2010

Health and Safety at Work Act 2015

New Zealand Electrical Codes of Practice available at www.worksafe.govt.nz;

and all subsequent amendments and replacements.

4	Definitions

Industry practice – those practices that competent practitioners within the industry recognise as current industry best practice.

Significant electrical installations – industrial, commercial, residential, or domestic installations involving a minimum of: lighting and power subcircuits, main switchboard, mains supply, and earthing system and that may require inspection by a registered electrical inspector.

5	Commissioning processes associated with electrical installations includes – all tests, adjustments, inspections, and related activities necessary to bring previously installed electrical equipment and systems into service.

6	Range

a	All aspects of evidence must comply with the legislation, codes of practice, and standards listed in Guidance Information note 3.

b	Hardware is to include all hardware in the installation and may include motors, drives, machinery control centres, distribution panels.

Outcomes and performance criteria

Outcome 1

Demonstrate knowledge of standard commissioning procedures and documentation used to manage significant electrical installations.

Performance criteria

1.1	Site-specific safety requirements are acknowledged in accordance with industry practice.

1.2	Commissioning schedules are explained in accordance with specifications, objectives, and industry practice.

Range	may include but is not limited to – manual systems; software such as spreadsheets, project management software.

1.3	Progress reporting, handover procedures, and check sheets are explained in accordance with industry practice.

1.4	Inspection forms and their uses are explained.

Range	wiring and connection, hardware, software.

1.5	The requirement for liaison with stakeholders is explained to ensure effective coordination of commissioning activities in accordance with industry practice.

Range	stakeholders may include but are not limited to – other project managers, accountant, site managers, engineers, technical experts, IT providers, supervisors, safety coordinators, suppliers, contractors.

1.6	Procedures and documentation requirements of commissioning significant remotely-controlled electrical installations are explained in accordance with industry practice.

Outcome 2

Design and develop a documentation pack for commissioning and handover of a significant electrical installation.

Performance criteria

2.1	Documentation pack is designed and developed for a given significant electrical installation in accordance with industry practice.

Range	inspection forms, wiring, hardware, software, remotely-controlled installation, sign off sheet and handover check sheet.

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 19 June 2009 | 31 December 2025 |
| Rollover and Revision | 2 | 15 March 2012 | 31 December 2025 |
| Revision | 3 | 15 January 2014 | 31 December 2025 |
| Rollover and Revision | 4 | 28 January 2021 | 31 December 2025 |
| Review | 5 | 27 April 2023 | 31 December 2025 |

| Consent and Moderation Requirements (CMR) reference | 0003 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.