| Title | Operate an aircraft hi-lift cabin service vehicle |
| --- | --- |
| Level | 3 | Credits | 7 |

| Purpose | People credited with this unit standard are able to: carry out safety checks; drive an aircraft hi-lift cabin service vehicle and dock with an aircraft; and undock a hi-lift cabin service vehicle from an aircraft. |
| --- | --- |

| Classification | Aviation > Ramp Operations |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

| Prerequisites | Persons seeking credit for this unit standard must hold a current Airside Driving Permit. |
| --- | --- |

Guidance Information

1	All tasks are to be carried out in accordance with enterprise procedures, the enterprise being the organisation carrying out the work.  Enterprise procedures referred to in this unit standard are the applicable procedures found in the following:

enterprise exposition; manufacturer publications; Government and local body legislation; airworthiness authority requirements.

2	Range

Vehicle type may include – cleaning truck, catering truck, disabled passenger lifter (Ambulift).

Outcomes and performance criteria

Outcome 1

Carry out safety checks.

Performance criteria

1.1	Visual check for damage to vehicle is undertaken.

Range	may include but is not limited to – body work, leaks under vehicle, tyres, lights.

1.2	Condition of vehicle is physically checked.

Range	may include but is not limited to – tyre pressure and condition, brake operation, fluid levels, fuel/charge level, steering operation, gear lever operation, lights, horn, FOD bin.

1.3	Any faults and malfunctions to the vehicle are identified and reported.

Outcome 2

Drive an aircraft hi-lift cabin service vehicle and dock with an aircraft.

Performance criteria

2.1	Vehicle controls are identified and used.

Range	start controls, drive control, direction control, release and apply park brake, lights, indicators.

2.2	Speed limits are adhered to in accordance with airport authority.

Range	may include but is not limited to – within 15 metres of an aircraft, within 15 metres of a fixed object or building, on the airport road network, general apron area.

2.3	Travel path and procedure for approaching an aircraft is followed.

Range	may include but is not limited to – anti-collision lights, other equipment and/or personnel in area, approach speed, remained clear of restricted areas, lifting deck fully lowered.

2.4	Procedure for docking with an aircraft is followed in accordance with aircraft type.

Range	may include but is not limited to – brake tests, use of stabilisers, height adjustments, alignment with aircraft, use of guide person.

2.5	Procedure for safe opening of aircraft doors is described and followed in accordance with aircraft type.

Range	may include but is not limited to – use of fall arrest systems, deployment of safety barriers, door opening procedures.

Outcome 3

Undock a hi-lift cabin service vehicle from an aircraft.

Performance criteria

3.1	Vehicle is undocked from the aircraft.

Range	may include but is not limited to – aircraft doors closed, door surrounds checked for damage, safety barriers retracted, loading deck cleared and lowered.

3.2	Procedures and travel path when leaving the aircraft are followed.

This unit standard is expiring. Assessment against this standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 16 October 2009 | 31 December 2018 |
| Review | 2 | 16 March 2017 | 31 December 2024 |
| Review | 3 | 27 October 2022 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0125 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.